## Slide 1: Runtime-Quality Tradeoff in Partitioning Based Multithreaded Packing
Dries Vercruyce
Elias Vansteenkiste and Dirk Stroobandt
Dries.Vercruyce@UGent.be
FACULTY OF ENGINEERING AND ARCHITECTURE

## Slide 2: Toolflow
FPGA configuration
HDL description
Synthesis
Technology mapping
Placement
Routing
Packing
Packing

## Slide 3: Packing
Seed based | Partitioning based
Bottom-up approach Seed block Affinity metric | Top-down approach Hierarchical partitioning of the circuit
Fast Tight packing | Slow Constraints
Local minima No multithreading | Quality of results Multithreading
Notes: Once a circuit is split in half, we thread both subcircuits independently during partitioning. This leads to the opportunity of multithreading.
QoR Wirelength and channelwidth

## Slide 4: Constraints
Local interconnect
LUT
FF
BLE
Fixed # input pins
Complete/sparse crossbar
Fixed # LUT/FF

## Slide 5: Related work
Constraints enforcing step required
Simplified architectures

## Slide 6: Contributions

## Slide 7: Contributions
No constraints enforcing step required
Fast multithreaded packing
  Multithreaded seed based packing (MultiPart)
Realistic heterogeneous architectures (MultiPart)

## Slide 8: Outline
Packing
Contributions
Circuit partitioning
PartSA
MultiPart
Experiments
Conclusions and Future work

## Slide 9: Circuit partitioning
A
B
MULT
FF
FF
FF
FF
FF
FF
LUT
LUT

## Slide 10: Circuit partitioning
A
B

## Slide 11: PartSA
Clustering based on design hierarchy
Simulated annealing fine-tuning cost function
N
1
1
1
1
1
1
1
1
1

## Slide 12: Simulated annealing: cost function

## Slide 13: Simulated annealing: cost function
Chart: PC
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 4 | 9 | 16 | 25
PTH
PMAX

## Slide 14: Problem: cutting critical paths

## Slide 15: Problem: cutting critical paths
Wedge
Wedge

## Slide 16: Problems with PartSA
Chart: Partitioning runtime [s]
| 4.9002509 | 1.889368800000001 | 0.7867414 | 0.3675995 | 0.7054984 | 1.46 | 1.299642560000001 | 0.63 | 0.7932609 | 1.977438100000001 | 1.110144 | 2.843800000000002 | 1.781386999999995 | 2.229197000000006 | 1.984818999999998 | 4.035502652863145 | 6.654397347136825 | 11.9358
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 14.94 | 16.229 | 16.81 | 17.814
Partitioning runtime increases as you go deeper in the hierarchy
Unused threads on first hierarchy levels
Large amount of subcircuits

## Slide 17: Problems with PartSA
Infeasible due to the large amount of required swaps
Partitioning runtime increases as you go deeper in the hierarchy
Hard to target commercial architectures
Commercial architectures contain sparse local interconnect crossbars
Detailed routing required in kernel of simulated annealing
Legal solution after block swap?

## Slide 18: MultiPart
No partitioning required on deep hierarchical levels
Detailed routing is feasible with seed based packing
Subcircuits are threaded independently
Multithreaded seed based packing

## Slide 19: Partition depth
Chart: Number of subcircuits after partitioning
| 2.0 | 4.0 | 6.0 | 8.0 | 10.0 | 12.0 | 14.0 | 16.0 | 18.0 | 20.0 | 22.0 | 24.0
 | 67.5881 | 65.3234 | 64.2685 | 63.9329 | 62.971 | 61.4538 | 61.0718 | 59.4903 | 59.0304 | 58.3933 | 58.4851 | 58.4445

## Slide 20: Problem: cutting critical paths
SDC File
Notes: Even though timing edges are added during partitioning, there is a chance that a critical path is cut during partitioning.

## Slide 21: Experimental results
Notes: None of the packers shown before is able to pack the VTR benchmarks and is not publicly available.
All results are related to AAPack

## Slide 22: Total wirelength
Notes: Related to AAPack!

## Slide 23: Minimum channel width
Smaller and cheaper FPGA’s

## Slide 24: Execution time and scaling behaviour
Chart: Circuit area [x106]
| 0.151185 | 0.300205 | 0.327634 | 0.390412 | 0.77004 | 0.810068 | 1.404412 | 2.685931 | 3.380809 | 5.271193
AAPack | 3.7837 | 5.2387 | 3.7437 | 4.835 | 14.1713 | 21.1938 | 13.92 | 63.3667 | 72.1783 | 161.985
PartSA | 1.56 | 3.705 | 2.0217 | 3.6817 | 8.5783 | 11.18 | 10.5283 | 31.99 | 37.8667 | 69.088
MultiPart | 1.2688 | 2.7113 | 2.0238 | 2.5225 | 5.425 | 6.0775 | 5.4037 | 19.0475 | 25.0188 | 40.3675
Name | Area | Runtime speed-up | 
 |  | PartSA | MultiPart
LU8PEEng | 770K | 1.7x | 2.6x
LU32PEEng | 2.7M | 2x | 3.3x
LU64PEEng | 5.3M | 2.3x | 4x

## Slide 25: Summary
 | Total wirelength | Critical path delay | Runtime speed-up
K6_N10_40nm (complete crossbar) |  |  | 
PartSA | -26% | -1.5% | 1.8x
MultiPart | -12% | -2.6% | 2.7x
K6_N10_gate_boost_0.2V_22nm (sparse crossbar) |  |  | 
MultiPart | -20% | -3.7% | 2.9x

## Slide 26: Conclusion and future work
Partitioning based packing methods
    Design hierarchy preserved
    Multithreaded parallelism
Higher quality packing in less runtime
    Total wirelength
    Minimum channel width
    Critical path delay
Future work: Extend MultiPart Titan benchmark design suite

## Slide 27: Extra: Results for Titan
Chart: Total runtime [s]
| AAPack | MultiPart
Packing | 233.7749 | 68.9718
Placement | 397.5595 | 375.0438
Routing | 381.2859 | 235.5679
 | Total wirelength | Critical path delay | Runtime speed-up
VTR | -20% | -3.7% | 2.9x
Titan | -28% | -6% | 3.6x

## Slide 28: Acknowledgement
Supported by European Commission H2020-FETHPC EXTRA project:
The author is supported by a PhD grant of the Research Foundation Flanders (FWO)

## Slide 29: ADDITIONAL SLIDES

## Slide 30: Multithreaded partitioning
CPU with 4 cores