## Slide 1: Overcoming Resource Underutilization in Spatial CNN Accelerators
Yongming Shen, Michael Ferdman, Peter Milder
COMPAS Lab, Stony Brook University

## Slide 2: CNN on FPGAs
Convolutional Neural Networks (CNNs)
  Best known method for object recognition [Simonyan, ICLR2015]
  Massive amount of computation
  Highly parallel, amenable to hardware acceleration
FPGA-based CNN Acceleration
  Lots of compute units (DSP slices) Exploit parallelism
  Reconfigurable fabric CNN-tailored caches and dataflow
  Energy efficient
Conv. Layer 2
Conv. Layer 1
Conv. Layer 0
DOG

## Slide 3: The Underutilization Problem
Conv. Layer 2
Conv. Layer 0
Conv. Layer 1
45% Util.
100% Util.
100% Util.
State-of-the-art: whole FPGA  one processor [Zhang, FPGA2015]
  Single-CLP (Convolutional Layer Processor)
Dimension mismatch causes dynamic underutilization
  Part of the compute array becomes idle
  Only 74% average utilization with AlexNet on Virtex-7 485T
  Less than 30% average utilization on larger FPGAs (~10K DSP slices)
40% Util.
FPGA
CLP

## Slide 4: Our Multi-CLP Solution
Single large CLP  Multiple smaller CLPs
  Total DSP-slice consumption remains the same
Each CLP optimized for a subset of layers
Multiple images in flight at the same time
  Avoids data dependency between CLPs
AlexNet on Virtex-7 485T (simulation)
  74% util.  97% util., 1.3x speedup
AlexNet on FPGAs with ~10K DSP slices (model)
  30% util.  96% util., 3.2x speedup
FPGA
CLP
FPGA
CLP0
CLP1
CLP2