## Slide 1: Reconfigurable Circuit for Implementation of Family of 4-phase Latch Protocols
Jotham Vaddaboina Manoranjan, Kenneth S. Stevens
University of Utah
International Conference on Field-Programmable Logic and Applications, 2016

## Slide 2: Introduction
Relative Timing (RT) based asynchronous designs have shown 3x, 1.5x and 1.2x benefits in terms of energy, area and performance on ASICs
Current generation of FPGAs are not ideal for prototyping or implementing RT architectures
An Asynchronous FPGA (A-FPGA) can allow seamless prototyping and also transfer RT power-performance benefits to FPGA implementations

## Slide 3
Fig 1. 3-stage bundled data asynchronous pipeline

## Slide 4: Greatest Challenge: Controller Implementation on FPGA
Asynchronous circuits often require special circuit components, such as asynchronous controllers, forks and joins for the implementation
  These are usually Mealy state machines with combinational feedbacks
  Logic hazards and glitches must be avoided
  Behavior must be formally proven to be correct

## Slide 5
There are 158 4-phase latch protocols!!!

## Slide 6: Two Ways:
Soft Implementations LUT based implementations, no change in FPGA Different structure and timing characteristics for each Highly flexible, slower, higher power
Hard Implementations Custom controller for each protocol added to FPGA Different circuit for each protocol No flexibility, faster, lower power

## Slide 7
There are 158 4-phase latch protocols!!!

## Slide 8: Designed Circuit
LUT based configurability for protocol flexibility
Use of standard cell logic for state holding and signal paths, reducing power and improving performance
~3.5x benefit in energy per cycle compared to soft implementations

## Slide 9: Questions???? Come find me tomorrow 