## Slide 1: Annotation-Based Finite-State Transducers on Reconfigurable Devices
Raphael Polig, Kubilay Atasu, Christoph Hagleitner, Theresa Xu, Akihiro Nakayama
30 August 2016

## Slide 2: Agenda
Introduction
IBM Care Management Analytics
Accelerator Design
Results

## Slide 3: Text Analytics by example
(Reuters) - International Business Machines Corp said on Wednesday it had acquired AlchemyAPI, a fast-growing startup selling software that collects and analyzes unstructured text and data in ways big enterprises, website publishers and advertisers find useful.
…
Buyer | Target | Status
IBM | AlchemyAPI | Completed
Notes: Information extraction
Find entities
Create relations
Involves several NLP steps such as tokenization, PoS tagging, shallow parsing
Several tools, algorithms, libraries but most if not all create annotations

## Slide 4: Apache UIMA
Notes: Creates interoperability between different implementations
Specific set of process functions that the framework can call
Every annotator can have a Typesystem that defines what it produces
A type is somewhat of a struct that can inherit features of parent types

## Slide 5: Apache UIMA by example
Notes: Aggregate analysis engine
Made of primitives
One of them is the shallow parser we are talking about today that uses fine-state transducers

## Slide 6: Finite-State Transducers
np = Token[_unilex="DT"]|<E> . Token[_unilex="JJ"]* . Token[_unilex="NN"] | Token[_unilex="NNS"] ;
Notes: An FST is a finite-state machine with a set of states
And an input alphabet that allows it to transition from a set of initial states to a final state or match.
But it also has an output alphabet to create something while it transitions.
Set operations to set internal variables
Post operations to signal a valid data structure to the next FST or output
This creates FST cascades
The library we are using allows to write FST rules like this.
It is a bit like regular expressions over annotations.

## Slide 7: Shallow parsing
Notes: It can be used for shallow parsing which for example tries to find noun phrases
The POS tags are created by another processing step so the parser can make use of them to create this representation which makes it easier to see who barked

## Slide 8: Agenda
Introduction
IBM Care Management Analytics
Accelerator Design
Results

## Slide 9: IBM Care Management Analytics
Notes: IBM’s UIMA implementation plus a bunch of libraries to perfom NLP tasks
The advanced care insights team writes the rules to gain insight from patient records
This allows to gain insights from medical notes that are never stored in a structured form
Smoker? Heavy smoker?

## Slide 10: UIMA Processing Pipeline
Aggregate Analysis Engine
Lexical Annotator 1
Lexical Annotator 2
Shallow Parser 1
FST
Scanner
FST
FST
Scanner
FST
Notes: Let’s see how their processing pipelines look like
Always UIMA Aggregate Analysis Engines
One or more lexical analysis stages that perfom language detection, tokenization, POS tagging
One or more shallow parser stages
A single stage contains usually multiple so called scanners that are FST cascades and create a single final type of annotation such as a Number, Date, Medication

## Slide 11: Profiling results
Lexical Annotators PoS Tagging Dictionaries Tokenization
Shallow Parsers Finite State Transducers (FSTs)
55 to 95% of the execution time is spent on FSTs

## Slide 12: Agenda
Introduction
IBM Care Management Analytics
Accelerator Design
Results

## Slide 13: Concept
UIMA
PEAR
Partitioning and Hardware Synthesis
POWER8
CAPI
FPGA
Transformed
PEAR
Synthesized
FPGA logic
Notes: Starting from a PEAR file which combines all required files
Create FPGA logic for a set of selected scanners
Transform the descriptors in the PEAR file to make use of the FPGA

## Slide 14: Hierarchical partitioning
Lexical Annotator 1
Shallow Parser 1
Lexical Annotator 2
Shallow Parser 2
Hardware Parser
Shallow Parser*
Lexical Annotator 2
Lexical Annotator 1
Notes: Select the scanners to be offloaded
Reorder the remaining annotators
Create a new SW parser
Instantiate and configure the HW parser

## Slide 15: Overall system
Notes: Transfer required annotations

## Slide 16: Hardware layer
Type Decoder
Scanner Cascade
Type Multiplexer
FPGA Interface
(PSL/AFU)
Input Types
Output Types
Notes: Scanner cascade == parser

## Slide 17: Scanner – FST Cascade
FST Cascade
Input Types
Output Types
Finite State Machine
Controller
Enable
Signals
Multiplexer
select
signals
Notes: Every scanner node is a FST cascade and holds multiple FSTs
Enable once all input

## Slide 18: Example FST
State 5
State 6
State 7
State 8
State 9
Test Type1/
Set features
Test Type2/
Set Features
Test Type2/
Post Type4
Test Type1/
Post Type3

## Slide 19: State Transition Logic & Storage
Character start offset
Character end offset
Token start id
Token end id
Feature1
Feature2
Character start offset
Character end offset
Token start id
Token end id
Feature3
Feature4
Type1_i_d
Type2_i_d
Valid if (Type1_i_v & Active[5])
Valid if Type2_i_v & Active[6]
Active[7] = 1 if one of these conditions holds
Character start offset
Character end offset
Token start id
Token end id
Feature1
Feature2
Feature3
Feature4
Evaluate feature tests
Evaluate feature tests
Character start offset
Character end offset
Token start id
Token end id
Feature1
Feature3
Type3_i_d
Character start offset
Character end offset
Token start id
Token end id
Feature2
Feature4
Type4_i_d
Active[7]
Storage
for State7
Notes: Every state has registers that can capture the features that are set by incoming transitions and required by outgoing ones.
These are optimized if for example a feature is always forwarded

## Slide 20: Hardware Transition Logic

## Slide 21: Agenda
Introduction
IBM Care Management Analytics
Accelerator Design
Results

## Slide 22: Resource usage – Stratix V A7
Chart: 
| Heart | Medications | Smoking
M20Ks | 0.30547 | 0.37148 | 0.3207
ALMs | 0.52471 | 0.49685 | 0.48235
Target f = 100 MHz
Notes: Complete FPGA CAPI, AFU, Parser
More inputs, less complex FSTs

## Slide 23: Normalized processing time
Target f = 100 MHz
31x
5x
Notes: Processing time per kB
Parser only is up to 31x faster
End-to-end 3.8 to 5x

## Slide 24: Thank you!