## Slide 1
FMER: A Hybrid Configuration Memory Error
Recovery Scheme for Highly Reliable FPGA SoCs
Dimitris Agiakatsikas1,
Ediz Cetin2, Oliver Diessel1
School of Computer Science and Engineering1
School of Electrical Engineering and Telecommunications2

## Slide 2: Highly Reliable FPGA-based SoC designs
User and configuration bits of SRAM-based FPGAs are vulnerable to soft-errors
Error masking: SoC implemented of K interconnected TMR-subsystems (partitions)
a) TMR: Modules + Voters + I/O pins
b) TMR: Modules + Voters
  c) TMR: Modules

## Slide 3: Configuration memory error recovery
Scrubbing
    Energy wasting
    Increased MTTD
    Robust error recovery technique

## Slide 4: Configuration memory error recover
Module-based Error Recovery (MER)
  Low energy consumption
  Rapid MTTD
  No error recovery in the configuration frames of the support resources (shaded region)

## Slide 5: Configuration memory error recovery
FMER: A hybrid error recovery technique
  Errors in the conf. frames of the support resources (shaded area) recover with scrubbing
  Errors in the conf. frames of the modules recover with MER

## Slide 6: for years, : CREME96 GEO Peak 5-min. (= 2.66E-10), K = 5, T = 5 years

## Slide 7: Energy consumption, : CREME96 LEO Peak 5-min. (= 3.86E-13), K [1, 10], T = 5 years mission
SoC/Scrub (K = 5)
  WScrub = 50 seconds
  R(T) = 0.999
  E(T) = 30441 Joules
SoC / FMER (K = 5)
  WFMER = 219 seconds
  R(T) = 0.999
  E(T) = 110 Joules
  277X less energy than SoC/Scrub

## Slide 8: Conclusions
FMER: Achieves higher reliability than scrubbing or MER
FMER: Saves significant energy compared to scrubbing alone

## Slide 9: for years, : CREME96 LEO Peak 5-min. (= 3.86E-13), K = 5, T = 5 years, Wscrub= WFMER= 300 seconds
R(T)FMER = 0.99994
E(T)FMER = 2030 J
2.5X less energy than SoC/Scrub
R(T)Scrub = 0.994
E(T)Scrub = 5075 J

## Slide 10: Contributions
We propose FMER
We derive and compare the
  reliability
  availability
  energy consumption
of a TMR-based application SoC that utilizes either
  FMER
  or blind scrubbing
  or MER
  We show that SoC/FMER achieves the
  Highest Reliability and Availability
  Lowest energy consumption

## Slide 11: for sec., : 1000 x CREME96 GEO Peak 5-min. (= 2.66E-7), K = 5

## Slide 12: Design Formulation
FD : Device Conf.Frames (CFs)
: separates CFs devoted to the Support Resources (SRs) or the TMR modules
: separates CFs devoted to the TMR SRs or the SIMPLEX SRs
: mission duration
: failure rate of a configuration bit
: # TMR subsystems
: waiting time between scrub cycles

## Slide 13: Case study

## Slide 14: Results: System specifications
Device: Artix-7 (XC7A200T)
Configuration Speed: Maximum
The design is fully triplicated
# TMR subsystems: 5
TMR modules utilization: 70%
SRs utilization: 10%
CFs devoted to the TMR modules: 60% of the devices CFs
CFs devoted to the SRs : 40% of the devices CFs
Failure rate of a conf. bit: = 2.66E-10
Critical Bit Factor: CBF = 0.1
Mission Duration: 5 years

## Slide 15: for hours, : CREME96 GEO Peak 5-min. (= 2.66E-10), K = 5

## Slide 16: for years, : CREME96 GEO Peak 5-min. (= 2.66E-10), K = 5, T = 5 years
Wscrub= WFMER= 0 s, E(T)scrub= E(T)FMER= 8.2E7 Joules