## Slide 1: Ouessant: Microcontroller approach for flexible accelerator integration and control in System-On-Chip
Pierre-Henri Horrein, Benoit Porteboeuf, André Lalevée
Lab-STICC/Télécom Bretagne, Brest, France

## Slide 2: Context
Hardware implementation can be:
  Fast
  Energy efficient
  Scalable and reusable
Two main challenges:
  How do we develop?
  How do we access it from a large software application?
CPU
RAM
?
?
Software
(kernel, user code, …)
Accelerator
Accelerator

## Slide 3: Requirements
Main target: dataflow applications (software radio)
  Several applications on a single system
  Operation reuse
Hardware-agnostic integration
  Work should be done once
Transparency for application developer
Runtime reconfiguration capabilities
Low resource and time overhead
Availability

## Slide 4: Proposed solution: Ouessant
CPU
RAM:
Software code
Data (shared)
Ouessant microcode
Accelerator
Accelerator
System Bus
Controller:
Decodes instructions
Manage data transfers
Create direct connections
CPU

## Slide 5: Implementation status and results
Fully functional implementation
  Deployed on Xilinx FPGA with Leon3 and Zynq based SoCs
  3 operations available
Very low hardware footprint:
  Less than 950 LUTS and 800 Regs per accelerator
Usable under Linux (driver available shortly)
Automated generation of complete coprocessors
Available under an Open Source license at:
https://redmine.telecom-bretagne.eu/projects/ouessant