## Slide 1: Measure Twice and Cut Once: Robust Dynamic Voltage Scaling for FPGAs
Ibrahim Ahmed, Shuze Zhao, Olivier Trescases and Vaughn Betz
Email:ibrahim@ece.utoronto.ca
Notes: Do not read the title

## Slide 2: FPGA Power Consumption Challenge
Chart: Technology (nm)
| 150 | 130 | 90 | 65 | 40 | 28 | 14
 | 1.8 | 1.5 | 1.2 | 1.1 | 0.95 | 0.9 | 0.9

## Slide 3: FPGA Power Consumption Challenge
Chart: Technology (nm)
| 150 | 130 | 90 | 65 | 40 | 28 | 14
 | 1.8 | 1.5 | 1.2 | 1.1 | 0.95 | 0.9 | 0.9
VDD not scaling

## Slide 4: FPGA Power Consumption Challenge
Obstacle against entering emerging low power/mobile market (IoT)
Must show superior perf/W to compete in Data centers
Need innovation to bring power down
“The future of continued scaling is dependent on adaptive power management and voltage scaling”, IEEE Fellow Kevin Zhang, VP of Intel's Technology and Manufacturing Group

## Slide 5: Worst-case Modelling is Wasteful
Devices have different delay -> Variation !!

## Slide 6: Worst-case Modelling is Wasteful
Delay is temperature dependant
High
Temperature

## Slide 7: Worst-case Modelling is Wasteful
Delay is affected by VDD
Lower VDD

## Slide 8: Worst-case Modelling is Wasteful
Aging also affects delay
End-of-life

## Slide 9: Worst-case Modelling is Wasteful
Aging also affects delay
End-of-life
Static timing analysis (STA) accommodates the tail

## Slide 10: Worst-case Modelling is Wasteful
Aging also affects delay
End-of-life
Timing models add margins for :-
  Slow device
  Worst temperature
  Worst voltage droop
  End-of-life effects
  Guard-bands for noise, etc..

## Slide 11: How significant are the added margins ?
Chart: FIR filter Fmax on a 60-nm Cyclone IV (1.2 V nominal VDD)
| 850 | 900 | 950 | 1000 | 1050 | 1100 | 1150 | 1200 | 1250 | 1300 | 1350
Measured | 90 | 106 | 118 | 131 | 142 | 154 | 165 | 175 | 183 | 191 | 197
CAD | 115.19

## Slide 12: How significant are the added margins ?
Chart: FIR filter Fmax on a 60-nm Cyclone IV (1.2 V nominal VDD)
| 850 | 900 | 950 | 1000 | 1050 | 1100 | 1150 | 1200 | 1250 | 1300 | 1350
Measured | 90 | 106 | 118 | 131 | 142 | 154 | 165 | 175 | 183 | 191 | 197
CAD | 115.19
> 20 % reduction in VDD without reducing Fmax

## Slide 13: How significant are the added margins ?
Chart: FIR filter Fmax on a 60-nm Cyclone IV (1.2 V nominal VDD)
| 850 | 900 | 950 | 1000 | 1050 | 1100 | 1150 | 1200 | 1250 | 1300 | 1350
Measured | 90 | 106 | 118 | 131 | 142 | 154 | 165 | 175 | 183 | 191 | 197
CAD | 115.19
> 20 % reduction in VDD without reducing Fmax
Dynamic Voltage Scaling (DVS)

## Slide 14: Dynamic Voltage Scaling
Find minimum VDD that guarantees operation at required speed
VDD, reduces both dynamic and static power
DVS has been commercially adopted by CPUs, but not FPGAs
FPGA’s programmability  unknown critical path at fabrication time
This work: exploit programmability to perform design & chip-specific calibration
Pdynamic a VDD2
Static power drops even faster
Notes: Dynamic power is quadratic in Vdd.
Static power is a bit more vomplicated p_stat = V_DD * I_leak, I_leak most important two forms are subthreshold and junction leakage
usubthreshold is exponenetial in Vgs – Vth and Vds affects Vth (DIBL)
DVS is not a new idea, the concept is out there for some time.
Fpga programmability, i.e. un-kown critical path, hard to recover from errors (unlike CPUs)
We propose to leverage the FPGA programmability to our advantage, off-line calibration

## Slide 15: Outline
DVS proposal
Testing Procedure
FRoC
Results
Summary & Future work

## Slide 16: Outline
DVS proposal
Testing Procedure
FRoC
Results
Summary & Future work

## Slide 17: Conventional Design Cycle
Application
HDL
Application
bit-stream
FPGA
Program &
run application
with nominal
VDD
One Measurement by STA
Passes timing 

## Slide 18: DVS Proposal Overview
Critical
path
Application
HDL
CAD
System
Calibration
bit-stream
Application
bit-stream
FPGA
Replicated
critical
path
FPGA
Heaters
1st measurement by conventional STA (once per application)
Notes: First step, application runs through a CAD system that performs conventional synthesis, P&R, etc.. To generate the application bit-stream
The first measurement is done using the conventional static timing analysis which reports pessimistic paths delays, from which we can identify critical paths.
The CAD system also spits out a calibration bit-stream that identically replicates the application critical path + heaters+ testing logic.

## Slide 19: DVS Proposal Overview
Critical
path
CAD
System
Calibration
bit-stream
Application
bit-stream
FPGA
FPGA
Program & generate calibration table (CT)
2nd measurement by
on-chip calibration
(repeated for each FPGA)
Application
HDL
Power
stage
VDD

## Slide 20: DVS Proposal Overview
CAD
System
Calibration
bit-stream
Application
bit-stream
FPGA
FPGA
Program & generate calibration table (CT)
Program &
run application
with DVS
CT
Application
HDL
Power
stage
VDD

## Slide 21: DVS Proposal Overview
CAD
System
Calibration
bit-stream
Application
bit-stream
FPGA
FPGA
Program & generate calibration table (CT)
Program &
run application
with DVS
CT
Today’s talk
Application
HDL

## Slide 22: Generating the Calibration Bit-stream
Performed on each FPGA at least once
For aging effects, calibration with every
power up
Capture all speed-limiting paths
Invisible to FPGA users
Fast
Robust
Automated Calibration
FRoC CAD tool

## Slide 23: Outline
Motivation
DVS proposal
Testing Procedure
FRoC
Results
Summary & Future work

## Slide 24: How to measure Fmax
Stimulate with random inputs and check output ?
  Does not guarantee exercising the critical path (CP)
To robustly measure the delay of a path :-
  Off-path inputs must have a steady non-controlling value
LUT
Tested path
Steady 1/0

## Slide 25: How to measure Fmax
Stimulate with random inputs and check output ?
  Does not guarantee exercising the critical path (CP)
To robustly measure the delay of a path :-
  Off-path inputs must have a steady non-controlling value
  Control over the edge transition from input  output
LUT
Tested path
Edge
1/0
/

## Slide 26: Measuring the Delay of a Single Path
FF
LUT
FF
FF
FF
FF
LUT
LUT
LUT
FF
FF
FF
LUT
LUT
FF
Application
Replicate
Critical
path
(CP)

## Slide 27: Measuring the Delay of a Single Path
FF
LUT
FF
FF
FF
FF
LUT
LUT
LUT
FF
FF
FF
LUT
LUT
FF
Critical
path (CP)
Replicate
Application

## Slide 28: Measuring the Delay of a Single Path
FF
LUT
FF
FF
FF
FF
LUT
LUT
LUT
FF
FF
FF
XOR
XOR
FF
Critical
path
(CP)
Application
Change LUT mask

## Slide 29: Measuring the Delay of a Single Path
FF
LUT
FF
FF
FF
FF
LUT
LUT
LUT
FF
FF
FF
XOR
XOR
FF
Critical
path
(CP)
Application
Edge1
Edge2
Control edge
transition

## Slide 30: Measuring the Delay of a Single Path
FF
LUT
FF
FF
FF
FF
LUT
LUT
LUT
FF
FF
FF
XOR
XOR
FF
Critical
path
(CP)
Application
FF
XNOR
FF
Error
Error
detection
Edge1
Edge2
Detect timing faults
Input stimulus

## Slide 31: A Single Path Delay is Not Robust
Many paths have delay close to the CP
Within-die variation may cause some other paths to be more critical
Varying VDD affects FPGA elements delay differently
Robust; measure delay of many near critical paths
Fast; use 1 calibration bit-stream
Notes: Measuring Fmax of an application by measuring only 1 cp is not robust
Many paths are very close to the cp delay
On-chip variation may cause some other parts to be more critical
Delay of RE and LE change differently with changing Vdd
This means that we must test many near critical paths that may overlap. ---- > robustness

## Slide 32: Testing Disjoint Paths
Testing many disjoint paths is mostly easy
Repeat the same procedure for single path testing
Application
FF
FF
FF
FF

## Slide 33: Testing Disjoint Paths
Testing many disjoint paths is mostly easy
Repeat the same procedure for single path testing
Application
FF
FF
FF
FF
Calibration
FF
FF
FF
FF
Error
Error

## Slide 34: ..but What to Do with Overlapping Paths?
LUT
A
FF
S1
FF
S2
LUT
B
LUT
C
FF
Path1
Path2
Paths sharing a LUT through different inputs

## Slide 35: ..but What to Do with Overlapping Paths?
LUT
A
FF
S1
FF
S2
LUT
B
LUT
C
FF
Path1
Path2
Paths sharing a LUT through different inputs
To test Path1, fix off-path input at C

## Slide 36: ..but What to Do with Overlapping Paths?
LUT
A
FF
S1
FF
S2
LUT
B
LUT
C
FF
Path1
Path2
Paths sharing a LUT through different inputs
To test Path1, fix off-path input at C
Path1 & Path2 can’t be tested together

## Slide 37: ..but What to Do with Overlapping Paths?
LUT
A
FF
S1
FF
S2
LUT
B
LUT
C
FF
Path1
Path2
Paths sharing a LUT through different inputs
To test Path1, fix off-path input at C
Path1 & Path2 can’t be tested together
Need 2 separate test phases

## Slide 38: ..but What to Do with Overlapping Paths?
LUT
A
FF
S1
FF
S2
LUT
B
LUT
C
FF
Path1
Path2
Paths sharing a LUT through different inputs
To test Path1, fix off-path input at C
Path1 & Path2 can’t be tested together
Need 2 separate test phases
-Add Fix control signals to keep LUT output constant
-Test controller cycles through test phases sequentially
FixB
FixA

## Slide 39: LUT Masks for Testing
only added when required
Developed more LUT masks to test Cyclone IV carry-chains with the same controllability
K-LUT
Fix off-path inputs
Break re-convergent fan-outs
Control edge transition

## Slide 40: Can’t Test Everything with 1 Bit-stream
One or two LUT inputs used as control signals
LUT
P1
P2
P3
P4

## Slide 41: Can’t Test Everything with 1 Bit-stream
One or two LUT inputs used as control signals
LUT
P1
P2
Fix
Edge

## Slide 42: Can’t Test Everything with 1 Bit-stream
One or two LUT inputs used as control signals
Fixing LUT output does not break all re-convergent fan-outs
LUT
A
LUT
B
LUT
C
Path2
Path1
LUT
P1
P2
Fix
Edge

## Slide 43: Can’t Test Everything with 1 Bit-stream
One or two LUT inputs used as control signals
Fixing LUT output does not break all re-convergent fan-outs
LAB inputs constraint
Carry-chains constraints
LUT
A
LUT
B
LUT
C
Path2
Path1
LUT
P1
P2
Fix
Edge

## Slide 44: Outline
Motivation
DVS proposal
Testing Procedure
FRoC
Results
Summary & Future work

## Slide 45: CAD System with FRoC
Application
HDL
Quartus
P&R
Quartus
STA
FRoC
Calibration
HDL
Location &
Routing
Constraints
Quartus
Calibration
bit-stream
Application
bit-stream
Proposed CAD system
1) Paths selection
2) Paths replication
3) Grouping replicated paths
4) Test controller generation

## Slide 46: 1) Path selection
FF
LUT
FF
FF
FF
LUT
LUT
FF
Application circuit

## Slide 47: 1) Path selection
Extract near critical paths from STA
  {P1, P2, P3, P4, P5}
FF
4-LUT
FF
FF
FF
4-LUT
4-LUT
FF
Application circuit
P1
P2
P3
P4
P5

## Slide 48: 1) Path selection
Extract near critical paths from STA
  {P1, P2, P3, P4, P5}
Select which paths to test
  Can’t test {P2,P3,P4} in 1 bit-stream
FF
4-LUT
FF
FF
FF
4-LUT
4-LUT
FF
Application circuit
P1
P2
P3
P4
P5
Two inputs reserved for control signals (Fix , Edge)

## Slide 49: 1) Path selection
Extract near critical paths from STA
  {P1, P2, P3, P4, P5}
Select which paths to test
  Can’t test {P2,P3,P4} in 1 bit-stream
  Select the more critical paths
  {P1, P2, P3 , P5}
FF
4-LUT
FF
FF
FF
4-LUT
4-LUT
FF
Application circuit
P1
P2
P3
P5

## Slide 50: 2) Path replication
FF
4-LUT
FF
FF
FF
4-LUT
4-LUT
FF
Application circuit
P1
P2
P3
P5
Replication
+
Control Signals

## Slide 51: 2) Path replication
FF
4-LUT
FF
FF
FF
4-LUT
4-LUT
FF
Application circuit
P1
P2
P3
Replicated Paths
P5
FF
4-LUT
FF
FF
4-LUT
4-LUT
FF
Fix1
Edge1
Fix2
Edge2
Fix3
Edge3
Replication
+
Control Signals
P5
P1
P2
P3

## Slide 52: 3) Grouping replicated paths
Replicated Paths
FF
4-LUT
FF
FF
4-LUT
4-LUT
FF
Fix1
Edge1
Fix2
Edge2
Fix3
Edge3
P5
P1
P2
P3

## Slide 53: 3) Grouping replicated paths
Replicated Paths
FF
4-LUT
FF
FF
4-LUT
4-LUT
FF
Fix1
Edge1
Fix2
Edge2
Fix3
Edge3
P5
P1
P2
P3
Minimising test phases -> minimises calibration time

## Slide 54: 3) Grouping replicated paths
Replicated Paths
FF
4-LUT
FF
FF
4-LUT
4-LUT
FF
Fix1
Edge1
Fix2
Edge2
Fix3
Edge3
P5
P1
P2
P3
Minimising test phases -> minimises calibration time
Graph coloring problem

## Slide 55: 3) Grouping replicated paths
Replicated Paths
FF
4-LUT
FF
FF
4-LUT
4-LUT
FF
Fix1
Edge1
Fix2
Edge2
Fix3
Edge3
P5
P1
P2
P3
Minimising test phases -> minimises calibration time
Graph coloring problem

## Slide 56: 3) Grouping replicated paths
Replicated Paths
FF
4-LUT
FF
FF
4-LUT
4-LUT
FF
Fix1
Edge1
Fix2
Edge2
Fix3
Edge3
P5
P1
P2
P3
Minimising test phases -> minimises calibration time
Graph coloring problem

## Slide 57: 3) Grouping replicated paths
Replicated Paths
FF
4-LUT
FF
FF
4-LUT
4-LUT
FF
Fix1
Edge1
Fix2
Edge2
Fix3
Edge3
P5
P1
P2
P3
Minimising test phases -> minimises calibration time
Graph coloring problem

## Slide 58: 3) Grouping replicated paths
Replicated Paths
FF
4-LUT
FF
FF
4-LUT
4-LUT
FF
Fix1
Edge1
Fix2
Edge2
Fix3
Edge3
P5
P1
P2
P3
Minimising test phases -> minimises calibration time
Graph coloring problem
Tested > 5000 paths using 17 phases only !!

## Slide 59: 4) Test controller generation
For each test phase :-
  Set the appropriate control signals
  Generates input stimulus
  Detects timing faults
Test Controller
Replicated
paths
Input stimulus
Sink
registers
Control
signals
Error

## Slide 60: Outline
Motivation
DVS proposal
Testing Procedure
FRoC
Results
Summary & Future work

## Slide 61: Benchmarks & Target Chip
Dual-channel 51-tap low pass FIR filter
Full crossbar (Xbar) with 16 100-bit-wide-ports
Targeting Cyclone IV EP4CE115F29C7 (TSMC 60-nm technology)
Nominal VDD 1.2 V
Application | LE utilization | Reported FMAX
FIR filter | 67,505 (59 %) | 121 MHz
Crossbar | 26,579 (23 %) | 115 MHz

## Slide 62: How Many Edges Are We Covering ?
Timing edge is a connection between
  I & O of a cell (Cell delay) , O of a cell & I of another cell (connection delay)
Timing edge criticality = (longest path using this edge)/(CP delay)
Covering more than 90 % of the more critical bins.
FRoC favours testing the more critical edges
Criticality %
Timing edge coverage
Xbar 10000 candidate paths
FIR 10000 candidate paths

## Slide 63: First, a Sanity Check
Need to validate the CT values
Selected benchmarks are feed-forward applications with no buried states
L
F
S
R
Application
M
I
S
R
BIST controller
Ref
Tested
=
Chart: Supply Voltage (mV)
| 850 | 900 | 950 | 1000 | 1050 | 1100 | 1150 | 1200 | 1250 | 1300 | 1350
FIR measured Fmax | 90 | 106 | 118 | 131 | 142 | 154 | 165 | 175 | 183 | 191 | 197
CAD | 115.19
Xbar measured Fmax | 89 | 104 | 118 | 131 | 144 | 157 | 168 | 178 | 187 | 195 | 203
 | 121.18

## Slide 64: How Many Paths to Measure ?
Chart: VDD(V)
| 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25
1 Path | 95 | 110 | 124 | 138 | 151 | 163 | 174 | 184 | 194
2000 Paths | 91 | 105 | 119 | 133 | 145 | 157 | 168 | 178 | 187
10000 Paths | 91 | 105 | 119 | 132 | 144 | 156 | 167 | 176 | 186
Benchmark Actual Fmax | 90 | 106 | 118 | 131 | 142 | 154 | 165 | 175 | 183
FIR
Chart: VDD(V)
| 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25
1 Path | 99 | 115 | 131 | 146 | 160 | 173 | 185 | 195 | 204
2000 Paths | 97 | 113 | 128 | 143 | 157 | 169 | 180 | 189 | 197
10000 Paths | 96 | 113 | 128 | 142 | 155 | 167 | 178 | 187 | 195
Benchmark Actual Fmax | 89 | 104 | 118 | 131 | 144 | 157 | 168 | 178 | 187
Xbar
Fan-out loading effects
1 path is not robust

## Slide 65: Fan-out Correction & Guard-banding
Correcting for fan-out through the difference in reported delay (by Quartus STA) between the calibration and the application bit-streams
  1 % for FIR & 5 % for Xbar
Guard-banding for IR-drop, crosstalk effects
  5 % for both benchmarks (experimental values)

## Slide 66: Generated CT & Power Savings
FIR
Xbar
Chart: VDD(V)
| 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25
Benchmark Actual Fmax | 90 | 106 | 118 | 131 | 142 | 154 | 165 | 175 | 183
Guard-banded CT | 85.54 | 98.7 | 111.86 | 124.08 | 135.36 | 146.64 | 156.98 | 165.44 | 174.84
Chart: VDD(V)
| 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25
Benchmark Actual Fmax | 89 | 104 | 118 | 131 | 144 | 157 | 168 | 178 | 187
Guard-banded CT | 86.4 | 101.7 | 115.2 | 127.8 | 139.5 | 150.3 | 160.2 | 168.3 | 175.5 | 181.8 | 186.3

## Slide 67: Generated CT & Power Savings
FIR
Xbar
Chart: VDD(V)
| 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25
Benchmark Actual Fmax | 90 | 106 | 118 | 131 | 142 | 154 | 165 | 175 | 183
Guard-banded CT | 85.54 | 98.7 | 111.86 | 124.08 | 135.36 | 146.64 | 156.98 | 165.44 | 174.84
 | 115.19
Chart: VDD(V)
| 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25
Benchmark Actual Fmax | 89 | 104 | 118 | 131 | 144 | 157 | 168 | 178 | 187
Guard-banded CT | 86.4 | 101.7 | 115.2 | 127.8 | 139.5 | 150.3 | 160.2 | 168.3 | 175.5 | 181.8 | 186.3
 | 121.18
Nominal operation
Nominal operation

## Slide 68: Generated CT & Power Savings
FIR
Xbar
Chart: VDD(V)
| 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25
Benchmark Actual Fmax | 90 | 106 | 118 | 131 | 142 | 154 | 165 | 175 | 183
Guard-banded CT | 85.54 | 98.7 | 111.86 | 124.08 | 135.36 | 146.64 | 156.98 | 165.44 | 174.84
 | 115.19
Chart: VDD(V)
| 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25
Benchmark Actual Fmax | 89 | 104 | 118 | 131 | 144 | 157 | 168 | 178 | 187
Guard-banded CT | 86.4 | 101.7 | 115.2 | 127.8 | 139.5 | 150.3 | 160.2 | 168.3 | 175.5 | 181.8 | 186.3
 | 121.18
Nominal operation
Nominal operation

## Slide 69: Generated CT & Power Savings
FIR
Xbar
Chart: VDD(V)
| 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25
Benchmark Actual Fmax | 90 | 106 | 118 | 131 | 142 | 154 | 165 | 175 | 183
Guard-banded CT | 85.54 | 98.7 | 111.86 | 124.08 | 135.36 | 146.64 | 156.98 | 165.44 | 174.84
 | 115.19
Chart: VDD(V)
| 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25
Benchmark Actual Fmax | 89 | 104 | 118 | 131 | 144 | 157 | 168 | 178 | 187
Guard-banded CT | 86.4 | 101.7 | 115.2 | 127.8 | 139.5 | 150.3 | 160.2 | 168.3 | 175.5 | 181.8 | 186.3
 | 121.18
Nominal operation
Nominal operation
With DVS, run both application safely at 1 V
Save > 33 % total power consumption

## Slide 70: Outline
Motivation
DVS proposal
Testing Procedure
FRoC
Results
Summary & Future work

## Slide 71: Summary
Presented a DVS approach tailored for FPGA (off-line calibration)
Created FRoC tool to automate the calibration procedure
Achieve more than 33 % total power reduction

## Slide 72: Future Work
Reducing guard-bands to enable more power savings
  Complete fan-out modelling for tested paths
  Account for IR-drop during calibration
# of required calibration bit-streams for full coverage
Testing hard blocks to find the safest minimum VDD

## Slide 73: Summary
Presented a DVS approach tailored for FPGA (off-line calibration)
Created FRoC tool to automate the calibration procedure
Achieve more than 33 % total power reduction