## Slide 1: Time-borrowing platform in the Xilinx UltraScale+ family of FPGAs and MPSoCs Ilya Ganusov, Benjamin Devlin

## Slide 2: Agenda
Time-borrowing concept
Hardware support for time-borrowing in UltraScale+
Time-borrowing algorithm based on ILP
Experimental results
Conclusion

## Slide 3: Time-borrowing
Improve Fmax by redistributing slack between fast and slow paths
Uneven slack arises from
  Different logic depth
  Quantized routing
  Point-to-point vs high-fanout connectivity
  Control sets, routing congestion, and other PNR restrictions

## Slide 4: Time Borrowing based on Clock Skew Scheduling
CRITICAL SETUP
PATH
JUST MEETS

## Slide 5: Time Borrowing based on using pulsed latches
CRITICAL SETUP
PATH
JUST MEETS

## Slide 6: Time Borrowing and Re-timing
Time-borrowing
Re-timing
Practical differences
 | Re-timing | Time-borrowing
Transparency to user | Invasive netlist changes | No design changes
Granularity | Coarse | Fine-grain
Sensitivity to control sets (CE/RST) | Sensitive | Insensitive
Max WNS change | ∞ | HW-defined
*
*Sapatnekar and Deokar, Utilizing the retiming-skew equivalence in a practical algorithm for retiming large circuits, CAD 1996

## Slide 7: Agenda
Time-borrowing concept
Hardware support for time-borrowing in UltraScale+
Time-borrowing algorithm based on ILP
Experimental results
Conclusion

## Slide 8: UltraScale+ MPSoC Floorplan
Programmable delays and pulse generators

## Slide 9: Programmable Delay Hardware
Location
  Junction between distribution and leaf clocking
Quantity
  One per leaf clock track
  16 time-borrowing blocks per 960 FFs
Features
  5 clock delay taps + pulse generator
  Cascading for cost-efficient way of borrowing > 300ps

## Slide 10: Clock Skew Scheduling and Pulsed Latches
Baseline leaf clock bypasses programmable delays
Bypass logic optimized for latency (minimizes extra variation, jitter)
Clock skew scheduling
Pulsed latches
FF

## Slide 11: Agenda
Time-borrowing concept
Hardware support for time-borrowing in UltraScale+
Time-borrowing algorithm
Experimental results
Conclusion

## Slide 12: Software flow
Many strategies possible
  Use a subset of skews/pulse widths: minimize runtime
  Use all features, violate hold and fix with hold router: maximize Fmax
Time-borrowing algorithms
  Local greedy optimization
  Globally optimal ILP-based
This work (Vivado 2016.1)
  Do not violate hold
  Globally optimal ILP solution
synthesis
place
route
bitgen
Time-borrowing optimization

## Slide 13: Time Borrowing Based on Global ILP algorithm
Extracting timing subgraph
  Max paths
  Min paths
Construct LP constraints for each path
  Setup:
  Hold:
  Objective function:
Extract timing subgraph
Construct LP formulation
LP solver
Deposit skew solution
report

## Slide 14: Full Set of ILP constraints
Setup constraint
Hold constraint
Clock delay variation
Pulse width variation
Clock skew delay tap/pulsed latch exclusivity

## Slide 15: Agenda
Time-borrowing concept
Hardware support for time-borrowing in UltraScale+
Time-borrowing algorithm
Experimental results
Conclusion

## Slide 16: Experimental setup
Vivado Design Suite version 2016.1
≈90 representative designs and Xilinx IP blocks
  Communications, test/measurement, emulation, etc
Implemented on UltraScale+ devices
  Fastest speed grade -3E
Metric | Min | Max | Avg
clk domains | 1 | 28 | 2
FMax | 77 MHz | 850 MHz | 300 MHz
LUT | 8k | 464k | 129k
FF | 3k | 586k | 123k
BRAM | 0 | 1152 | 187
DSP | 0 | 2700 | 195
Total designs | 89 |  | 

## Slide 17: Performance improvement results
Default time-borrowing configuration
  5 clock skew values [0, 41, 96, 168, 295]ps
  1 clock pulse width 295ps
Globally optimal ILP algorithm
  No hold violations allowed
Chart: Per-design performance improvements
Chart: geometric mean
| gmean Fmax increase (%)
pulsed latch | 0.8
clock skew scheduling | 5.1
pulsed latch + clock skew scheduling | 5.3

## Slide 18: Cascading programmable delays
Cost-efficient way to borrow > 300ps
  8 possible clock skew values [0, 41, 96, 168, 295][+295]*ps
  2 pulse widths [295, 610]ps
  No hold violations allowed
Chart: Per-design performance improvements
Chart: gmean Fmax increase (%)
| no cascade | cascade of 2
 | 5.4953 | 7.3919

## Slide 19: Hold Sensitivity Analysis
Impact of hold on Fmax
  5.5% Fmax with 0 hold violations
  router can potentially delay fast paths
  measure impact of adding hold margin
Results
- holdMargin
Chart: gmean Fmax increase (%)
| pulsed latch | clock skew scheduling | pulsed latch + clock skew scheduling
0ps | 0.8 | 5.1 | 5.3
41ps | 0.9 | 6.3 | 6.6
96ps | 1 | 6.8 | 7.5
168ps | 1.6 | 7.1 | 8.1
295ps | 5 | 7.2 | 8.5

## Slide 20: Location, cost, and performance
Why delay and replicate leaf clocks?
  Why not global clock buffers?
  Why not in the logic slice?
Replicated leaf architecture provides highest Fmax/$
Chart: relative UltraScale+ chip area
| 0.33095238095238089 | 0.45714285714285707 | 0.64523809523809517 | 1
leaf + n | 1.06 | 2.37 | 3.88 | 5.5
leaf + 0 | 0.71 | 1.58 | 2.23 | 3.22
slice | 1.22 | 2.87 | 4.81 | 7.16
1.3% Fmax/unit area
5% Fmax/unit area

## Slide 21: Concluding Remarks
UltraScale+ architecture with programmable time-borrowing
  improves Fmax by re-distributing slack between fast and slow paths
  employs both clock skew scheduling and pulsed latches
  transparent to customer, no netlist changes
Performance results in production (Vivado 2016.1)
  5.5% gmean Fmax increase with zero-hold ILP-based algorithm
  higher Fmax possible when using cascades or increasing hold margin
Area- and runtime-efficient
  Less than 0.1% of additional chip area
  Less than 4 minutes of additional runtime on average

## Slide 22: Thank you