## Slide 1: Accelerating particle identification for high-speed data-filtering using OpenCL on FPGAs and other architectures
for FPL 2016
Srikanth Sridharan
CERN
8/31/2016

## Slide 3: Background 1/2
Upgrades planned for LHCb exp. at CERN
  Capture 40M particle collisions per sec at LHCb
  Or a new collision every 25ns
  Generates data @40Tb/s
  Need to capture 100% of the data
  Currently capturing only 2.5%
  * Projections from High Throughput Computing Project Status Report 22/6/16 by Niko Neufeld
Chart: Projected Throughput [Tb/s]
| Alice (2019) | Atlas (2023) | CMS (2023) | LHCb (2019) | LHCb (today)
Throughput | 10 | 22 | 40 | 40 | 1

## Slide 4: Background 2/2
Need to process all data in large computing farm to reconstruct events
Impossible with just CPUs
Hence need for accelerators
FPGA attractive due to performance and power efficiency
OpenCL makes FPGAs more accessible

## Slide 5: Ring Imaging Cherenkov Detector (RICH) concept
  One of the sub detectors of LHCb
  Charged particles faster than light produce cone of Cherenkov photons
  Like the light equivalent of a sonic boom
  Reflected on spherical mirrors and captured on photodetectors
  Ring size ∝ Cherenkov angle
  * Detector Images from “RICH pattern recognition” Note LHCb-98-040 by Forty, R, and O Schneider
  Sonic boom image from http://strangesounds.org/wp-content/uploads/2013/08/sonic-boom.jpg

## Slide 6: RICH - Ring Imaging Cherenkov Detector 2/2
  Calculate Spherical reflection Point
  Calculate Cherenkov angles
  Cherenkov angle ∝ particle velocity-1
  Momentum and in turn Mass inferred from trajectory
  Particle type inferred from velocity and mass
  * Images from “RICH pattern recognition” Note LHCb-98-040 by Forty, R, and O Schneider

## Slide 7: RICH Particle Identification Algorithm
  50% of overall event reconstruction processes
  Cherenkov angle reconstruction – 20% of RICH
    Like inverse ray tracing in 3D space
    Spherical mirrors make it more complicated
    Solve system of Quadratic equations, cubic roots, matrix rotations, cross products and Eigen functions etc. in floating point
  Parallelizable for n particle
  Pipelinable

## Slide 8: OpenCL implementation
Start from an existing single threaded C++ implementation as reference
Create an OpenCL kernel from scratch
  Remove framework dependencies (Eg. Gaudi, Root)
  Recreate library function equivalents
  Datatype modifications (Eg. Gaudi::XYZPoint, Eigen3Vector etc.)
  Implement, Parallelize and optimize the algorithm

## Slide 9: Results of OpenCL implementation
Chart: Speed up based on OpenCL kernel runtimes
| 10000000 | 1000000 | 100000 | 10000
Nallatech 385 card with Stratix V FPGA | 54.15 | 53.25 | 51.6 | 37.9
Nvidia GeForce GTX690 card (normalized for 1x GPU) | 96.89 | 95.89 | 87.87 | 53.53
System with 2 Intel Xeon E5-2650 CPUs (normalized for 1x CPU) | 30.98 | 21.29 | 11.57 | 4.41
Reference: Intel Core i7-4770

## Slide 10: Performance per Watt
Metric | Devices |  |  | 
 | Stratix V FPGA | Nallatech 385 card with 1x Stratix V FPGA | Nvidia GeForce GTX 690 card with 2x GPU | 2x Intel Xeon E5-2650 CPU
Avg. Run-time for 10 Million Photons (μs) | 37017.44 | 37017.44 | 10345.13 | 32360.17
No. of Photons per microsecond (μs-1) | 270.14 | 270.14 | 966.64 | 309.02
Power consumption (W) | 21.27 (Profiled) | 25 (Typ. Max) | 300 (Max) | 190 (TDP)
Estimated No. of Photons per microsecond per Watt (μs-1W-1) | 12.70 | 10.81 | 3.22 | 1.63
Chart: Estimated No. of Photons / microsecond / Watt (μs-1W-1)
| Nallatech 385 card - 1x Stratix V FPGA (Based on profiled Power) | Nallatech 385 card - 1x Stratix V FPGA (Based on Typ. Max Power) | Nvidia GeForce GTX 690 card - 2x GPU (Based on Max Power) | Xeon E5-2650 -2x CPU (Based on TDP Power)
No. of Photons per microsecond per Watt (μs-1W-1) | 12.6991 | 10.8057 | 3.2221 | 1.6264

## Slide 11: But…when factoring data transfer
Chart: Speed up of OpenCL kernel time+ data transfer time over optimized Reference
| 10000000 | 1000000 | 100000 | 10000
Nallatech 385 card with Stratix V FPGA | 6.39 | 5.43 | 2.48 | 0.57
Nvidia GeForce GTX690 card (normalized for 1x GPU) | 4.69 | 4.65 | 3.77 | 2.72
System with 2 Intel Xeon E5-2650 CPUs (normalized for 1x CPU) | 2.52 | 2.82 | 1.46 | 1.03
Reference: Intel Core i7-4770

## Slide 12: AVENUES FOR IMPROVING OVERALL RUNTIME ON FPGA
1.Overlapping computation and data transfer
  Default case: Transfer time and kernel runtime for single blocking command queue
  Opt 1: 10 Command queues with 1/10th data each, non blocking with event waitlist
  Opt 2: Opt1 + flush after kernel

## Slide 13: Improvement in numbers
Comparison of speedup for Overlapping and non Overlapping transfers
Small improvement but 10x transfer adds 10x latency
Type of Commands in Command Queue | No of Photons | Global work size | Speedup
Blocking (Default case) | 1e7 | 1e7 | 6.39
Nonblocking, No flush (Opt 1) | 1e7 | 10x 1e6 | 6.02
Nonblocking, Flush after kernel (Opt 2) | 1e7 | 10x 1e6 | 5.99
Blocking (Default case) | 1e6 | 1e6 | 5.43

## Slide 14: 2. Increasing the compute units on the FPGA / moving to a different FPGA
FPGA resource usage
  DSPs – only resource heavily used
  FPGA on Nallatech card: Stratix V GX variant with only 256 DSP blocks
  Stratix V GS variants have 600-1963 DSP blocks
  Potential to 2X throughput by increasing Computational Units
Resource | % of Resource used by OpenCL design | 
 | Kernel | Total
LEs | 10.8525 % | 22.4216 %
FFs | 9.34081 % | 16.4616 %
RAMs | 11.4844 % | 26.9531 %
DSPs | 79.2969 % | 79.2969 %
Avg. Utilization | 19.4127 % | 36.9868 %
Move to Next gen FPGAs
  Hard Floating Point units
  Potentially could match GPU in raw performance

## Slide 15: Moving to a faster memory / low latency coherent memory access
3. Faster Memory
  GeForce GTX690 card: GDDR5 with bw of 384GB/s
  Nallatech FPGA card: DDR3 with bw of 25.6GB/s
4. Low latency coherent memory access
  Intel QPI, IBM CAPI
  ~100x lower latency than PCIe
  View of main memory
  Already see significant improvements

## Slide 16: 5. Relaxing the Host centric OpenCL model
Host CPU at center of OpenCL model
  Manages data transfers, kernel execution…
  Device cannot start execution unless host issues commands
  Add control latency on top of data latency
  Unavoidable with opaque interfaces like PCIe
Can be replaced under SVM context
  Device can schedule read and write by itself
  Command queues and event wait list exists, but managed by host
  Potential for device based command queues
  More autonomy for devices

## Slide 17: Conclusion
GPU has 1.8X better kernel performance over FPGA (normalized)
FPGA has 1.4X better overall performance over GPU (normalized)
FPGA has Order of magnitude better power efficiency & Performance/Watt
OpenCL – a game changer for FPGAs
  Accelerated development time
  ~2weeks for OpenCL vs ~2months for RTL