## Slide 1: Model-Based Optimization of High Level Synthesis Directives
Charles Lo, Paul Chow

## Slide 2: HLS Workflow
Directives
Code Changes
Functional C/C++ Code
Application
Tuned
HDL Module
void func(…)
{
int array_1 [1024];
int array_2 [512];
loop1: for (…)
loop2: for (…)
}

## Slide 3: HLS Generators
Directives
Code Changes
void func(…)
{
int array_1 [1024];
int array_2 [512];
loop1: for (…)
loop2: for (…)
}
Functional C/C++ Code
HLS Generator
High-Throughput
Implementation
Low-DSP
Implementation
Family of
Implementations

## Slide 4: Parameter Selection
set_directive_pipeline
-II <integer>
-enable_flush
-rewind
<location>
HLS Directives:
THIS WORK: Automatically select directives to tune an HLS design
for particular objective and constraints
Xilinx Complex Multiplier (6.0)
IP Generators:
Notes: HLS generators are given by the HLS environment,
Provide b

## Slide 5: Outline
Problem Formulation
Model-Based Optimization
Intra-Program Transfer
Results
Conclusions & Future Work

## Slide 6: Problem Formulation
LUT Utilization
Clock Period x Cycle Latency
Set of possible directive settings
Black Box: no model for and
Complex interaction dependent on HLS and CAD tool implementation
Expensive: evaluation of is slow
Accurate area, clock frequency requires FPGA CAD flow

## Slide 7: Sequential Model-Based Optimization
Expected Improvement:

## Slide 8: Constrained Optimization
Need a measure of distance between directive settings

## Slide 9: Relating Directive Options
set_directive_array_partition array_1 –factor 4
set_directive_array_partition array_2 complete
set_directive_pipeline loop_1
set_directive_unroll loop_2
set_directive_array_partition array_1 complete
set_directive_array_partition array_2 complete
set_directive_pipeline loop_2
Directive Setting 1
Directive Setting 2
set_directive_array_partition array_1 –factor 4
set_directive_array_partition array_2 complete
set_directive_pipeline loop_1
set_directive_unroll loop_2
set_directive_array_partition array_1 complete
set_directive_array_partition array_2 complete
set_directive_pipeline loop_2

## Slide 10: Directive Representation
myfunc array_1:
directives:
array_partition:
- disable
- enable:
type:
- complete
- block –factor 4
Design Space Description:
One-hot encoding:
4-D Vectors:
0110
Squared Exponential Kernel:
complete
enable

## Slide 11: Directive Reuse
void func(…)
{
int array_1 [1024];
int array_2 [512];
loop1: for (…)
loop2: for (…)
}
partition, reshape
unroll, pipeline
Idea: Application of a directive to different code structures has
similar effect
Transfer

## Slide 12: Relating Common Directives
set_directive_array_partition array_1 –factor 4
set_directive_array_partition array_2 complete
set_directive_pipeline loop_1
set_directive_unroll loop_2
set_directive_array_partition array_1 complete
set_directive_array_partition array_2 complete
set_directive_pipeline loop_2
Directive Setting 1
Directive Setting 2
set_directive_array_partition array_1 –factor 4
set_directive_array_partition array_2 complete
set_directive_pipeline loop_1
set_directive_unroll loop_2
set_directive_array_partition array_1 complete
set_directive_array_partition array_2 complete
set_directive_pipeline loop_2

## Slide 13: Intra-Program Transfer
“enable array partition”
Append distance function:
“disable array partition”
“partition array_2” or
“partition array_1”
Notes: Want to compare along new axis

## Slide 14: Experiment Setup
Three case studies from MachSuite [1]:
AES: 104, 976 points
Backpropagation: 23, 328 points
Radix Sort: 7, 776 points
Directives: loop pipeline, unroll, array partition
All design points evaluated to find global optima:
Vivado HLS 2015.4 HDL Evaluation
Target: Virtex 7 485T @ 200MHz
[1] B. Reagen et al., “MachSuite: Benchmarks for Accelerator Design and Custom Architectures,” IISWC 2014

## Slide 15: AES Design Space
30th percentile
50th percentile

## Slide 16: AES Unconstrained Optimization

## Slide 17: AES Constrained (50%) Optimization

## Slide 18: Effects of Intra-Program Transfer
Transfer provides general directions to explore
  Useful early in unconstrained problems
  Constrained problems require more accuracy
In AES outer loops don’t follow trends
  Pipelining an outer loop leads to unroll of inner loops
  Different behaviour breaks assumption of transfer
Experiment: Ungroup outer loops in transfer kernel of objective function

## Slide 19: AES Constrained (50%) Optimization Revisited

## Slide 20: Conclusions & Future Work
Conclusions:
Sequential Model-Based Optimization is effective in quickly optimizing HLS directives
Useful correlations exist between directives that can be exploited to improve optimization speed
Future Work:
Fine-tune relations between directives via source code analysis
Develop prior models to guide early optimization

## Slide 21: Thanks!
Questions?
Charles Lo
locharl1@eecg.toronto.edu