## Slide 1: XNoC: A Non-intrusive TDM Circuit-switched Network-on-Chip
Tuan D. A. Nguyen (1)
ECE Department, National University of Singapore, Singapore
Chair of Processor Design, Center for Advancing Electronics Dresden, TU Dresden, Germany
& Akash Kumar (2)

## Slide 2: Why TDM Circuit-switched?
Circuit-switched (CSw) vs. Packet-switched
  Better predictability in real-time embedded systems [1,2]
TDM vs. SDM
  Lower data latency, less complex switch and cheaper network interfaces/switches [3]
[1] Goossens, K. & Hansson, A., 2010. The aethereal network on chip after ten years: Goals, evolution, lessons, and future. In DAC, 2010 47th ACM/IEEE. pp. 306–311
[2] Liu, S., Jantsch, A. & Lu, Z., 2013. Analysis and evaluation of circuit switched NoC and packet switched NoC. In DSD, 2013 Euromicro Conference on. pp. 21–28
[3] Sparsø, J., Kasapaki, E. & Schoeberl, M., 2013. An area-efficient network interface for a TDM-based Network-on-Chip. In DATE 2013. pp. 1044–1047.
Notes: Circuit-switched (CSw) NoC is known to perform better than packet switched (PktSw) NoC in real-time embedded systems [5], [6]. Some researchers proposed hybrid PktSwCSw NoCs to inherit the advantages of both types such as [7], [8]. However, they do not provide much benefit in terms of cost-performance ratio and they break the composability of the system [5]. CSw NoCs are classified into Spatial Division Multiplexing (SDM) [9]–[11] or Time Division Multiplexing (TDM) [12]–[15] or both [16]. However, TDM is preferred to SDM because of lower data latency, less complex switch and cheaper network interfaces/switches (NIs/SWs) [17].

## Slide 3: TDM CSw NoC Centralized vs. Decentralized
Features | Centralized NoC [1,2,3] | Decentralized NoC [4,5]
Have global view of the network |  | ×
Change routing algorithm |  | ×
Allocate multi-slot path |  | ×
Setup multicast domain |  | ×
Reconfiguration Latency | × | 
Scalability | × | 
[1] Goossens, K., Dielissen, J. & Radulescu, A., Æthereal network on chip: concepts, architectures, and implementations. Design & Test of Computers, IEEE, 2005
[2] Hansson, A., Subburaman, M. & Goossens, K., 2009. aelite: A flit-synchronous network on chip with composable and predictable services. In DATE 2009
[3] Stefan, R.A., Molnos, A. & Goossens, K., 2014. dAElite: A TDM NoC supporting qos, multicast, and fast connection set-up. IEEE Transactions on Computer, 2014
[4] Liu, S., Jantsch, A. & Lu, Z., 2014. Parallel probe based dynamic connection setup in TDM NoCs. In DATE 2014
[5] Lusala, A.K. & Legat, J.-D., 2012. A SDM-TDM-Based Circuit-Switched Router for On-Chip Networks. ACM TRETS 2012
Notes: The disadvantages of using decentralized compared to centralized control unit in [15], [16] are (1) it cannot establish a multi-cast domain because the sender needs to wait for the acknowledged signals from all receivers to make sure that the paths are setup; the control units would become much more complex to handle the responses from the neighbors; (2) the routing algorithm cannot be changed at runtime unless the routers are partially reconfigurable; (3) it does not have the global view of the current state of the network to adapt to changes at runtime; (4) it only allocates one slot for one path at a time; there is no guarantee that the data in multi-time-slot path arrive at the destination in order.
- The most concerned problem of CSw NoC with centralized control unit is the path setup and tear-down overhead. They can be over 1000 clock cycles in [12] or about 100 cycles for one short path in [14]. Having a predictable path setup/teardown latency as low as possible is the first step in making it feasible to interleave multiple paths that share the same links and time slots. It is similar to the context switching in multithreaded software environment. Another drawback of conventional centralized control unit is scalability. For large NoCs with hundreds or even thousand of PEs, the reconfiguration process becomes a bottleneck. Moreover, having the control links span the whole network severely affects the timing of the design. One may insert the buffers along the links but it again increases the reconfiguration latency.

## Slide 4: Problem – Modify Connection
SW00
SW10
SW20
NI00
NI10
NI20
SW01
SW11
SW21
NI01
NI11
NI21
SW02
SW12
SW22
NI02
NI12
NI22
SW03
SW13
SW23
NI03
NI13
NI23
Notes: Modifying path. PEs are attached to NIs and are numbered after their SW. PE00→PE03 is the path from PE00 to PE03. There are 4 time slots represented by 4 arrows. One more time slot is requested for PE00→PE03 to increase the bandwidth.
the reconfiguration process in the aforementioned NoCs is based on the assumption that it does not overlap with the data transfer. This is not the case in a scenario when the user changes from a low quality video to a higher one. The bandwidth of the existing path needs to be adjusted as shown in Fig. 1. This example is elaborated in Section III-D

## Slide 5: Problem – Multicast with Feedback
SW00
SW10
SW20
NI00
NI10
NI20
SW01
SW11
SW21
NI01
NI11
NI21
SW02
SW12
SW22
NI02
NI12
NI22
SW03
SW13
SW23
NI03
NI13
NI23
Notes: Modifying path. PEs are attached to NIs and are numbered after their SW. PE00→PE03 is the path from PE00 to PE03. There are 4 time slots represented by 4 arrows. One more time slot is requested for PE00→PE03 to increase the bandwidth.
the reconfiguration process in the aforementioned NoCs is based on the assumption that it does not overlap with the data transfer. This is not the case in a scenario when the user changes from a low quality video to a higher one. The bandwidth of the existing path needs to be adjusted as shown in Fig. 1. This example is elaborated in Section III-D

## Slide 6: Contributions
Features | Centralized NoC [1,2,3] | Decentralized NoC [4,5]
Have global view of the network |  | ×
Change routing algorithm |  | ×
Allocate multi-slot path |  | ×
Setup multicast domain |  | ×
Reconfiguration Latency | × | 
Scalability | × | 
Features | [1,2,3] | [4,5] | XNoC
Controller | Centralized | Decentralized | Distributed
Multicast with aggregated feedback | × | × | 
Non-intrusive reconfiguration | × | × | 
Reconfiguration Latency | × |  | 
Scalability | × |  | 
[1] Goossens, K., Dielissen, J. & Radulescu, A., Æthereal network on chip: concepts, architectures, and implementations. Design & Test of Computers, IEEE, 2005
[2] Hansson, A., Subburaman, M. & Goossens, K., 2009. aelite: A flit-synchronous network on chip with composable and predictable services. In DATE 2009
[3] Stefan, R.A., Molnos, A. & Goossens, K., 2014. dAElite: A TDM NoC supporting qos, multicast, and fast connection set-up. IEEE Transactions on Computer, 2014
[4] Liu, S., Jantsch, A. & Lu, Z., 2014. Parallel probe based dynamic connection setup in TDM NoCs. In DATE 2014
[5] Lusala, A.K. & Legat, J.-D., 2012. A SDM-TDM-Based Circuit-Switched Router for On-Chip Networks. ACM TRETS 2012
Notes: The disadvantages of using decentralized compared to centralized control unit in [15], [16] are (1) it cannot establish a multi-cast domain because the sender needs to wait for the acknowledged signals from all receivers to make sure that the paths are setup; the control units would become much more complex to handle the responses from the neighbors; (2) the routing algorithm cannot be changed at runtime unless the routers are partially reconfigurable; (3) it does not have the global view of the current state of the network to adapt to changes at runtime; (4) it only allocates one slot for one path at a time; there is no guarantee that the data in multi-time-slot path arrive at the destination in order.
- The most concerned problem of CSw NoC with centralized control unit is the path setup and tear-down overhead. They can be over 1000 clock cycles in [12] or about 100 cycles for one short path in [14]. Having a predictable path setup/teardown latency as low as possible is the first step in making it feasible to interleave multiple paths that share the same links and time slots. It is similar to the context switching in multithreaded software environment. Another drawback of conventional centralized control unit is scalability. For large NoCs with hundreds or even thousand of PEs, the reconfiguration process becomes a bottleneck. Moreover, having the control links span the whole network severely affects the timing of the design. One may insert the buffers along the links but it again increases the reconfiguration latency.

## Slide 7: XNoC - Centralized
SW00
SW10
SW20
SW01
SW11
SW21
SW02
SW12
SW22
NI00
NI10
NI20
NI01
NI11
NI21
NI02
NI12
NI22
Centralized Controller
Processor

## Slide 8: Contributions
Features | [1,2,3] | [4,5] | XNoC
Controller | Centralized | Decentralized | Distributed
Multicast with aggregated feedback | × | × | 
Non-intrusive reconfiguration | × | × | 
Reconfiguration Latency | × |  | 
Scalability | × |  | 
[1] Goossens, K., Dielissen, J. & Radulescu, A., Æthereal network on chip: concepts, architectures, and implementations. Design & Test of Computers, IEEE, 2005
[2] Hansson, A., Subburaman, M. & Goossens, K., 2009. aelite: A flit-synchronous network on chip with composable and predictable services. In DATE 2009
[3] Stefan, R.A., Molnos, A. & Goossens, K., 2014. dAElite: A TDM NoC supporting qos, multicast, and fast connection set-up. IEEE Transactions on Computer, 2014
[4] Liu, S., Jantsch, A. & Lu, Z., 2014. Parallel probe based dynamic connection setup in TDM NoCs. In DATE 2014
[5] Lusala, A.K. & Legat, J.-D., 2012. A SDM-TDM-Based Circuit-Switched Router for On-Chip Networks. ACM TRETS 2012
Notes: The disadvantages of using decentralized compared to centralized control unit in [15], [16] are (1) it cannot establish a multi-cast domain because the sender needs to wait for the acknowledged signals from all receivers to make sure that the paths are setup; the control units would become much more complex to handle the responses from the neighbors; (2) the routing algorithm cannot be changed at runtime unless the routers are partially reconfigurable; (3) it does not have the global view of the current state of the network to adapt to changes at runtime; (4) it only allocates one slot for one path at a time; there is no guarantee that the data in multi-time-slot path arrive at the destination in order.
- The most concerned problem of CSw NoC with centralized control unit is the path setup and tear-down overhead. They can be over 1000 clock cycles in [12] or about 100 cycles for one short path in [14]. Having a predictable path setup/teardown latency as low as possible is the first step in making it feasible to interleave multiple paths that share the same links and time slots. It is similar to the context switching in multithreaded software environment. Another drawback of conventional centralized control unit is scalability. For large NoCs with hundreds or even thousand of PEs, the reconfiguration process becomes a bottleneck. Moreover, having the control links span the whole network severely affects the timing of the design. One may insert the buffers along the links but it again increases the reconfiguration latency.

## Slide 9: XSwitch
Switch
North
East
West
South
Local
Notes: Unlike the conventional 5-port switch which is implemented by multiplexers with configurable selectors, our XSwitch is designed from a different point of view. Fig. 4 depicts the architecture of our XSwitch. We make use of the intrinsic idea of FPGA in implementing digital circuits using arrays of small memory elements (MEs) (lookup-table in Xilinx FPGA). As shown in Fig. 4a, there is one set of N 5-input MEs per output direction per output bit. The inputs are
from the North, East, West, South and Local ports. They are connected to the asynchronous address read port of the ME. The output port, connected to the read data output, is therefore the result of any 5-input combinational circuit. Multiplexer is just one of them. Fig. 4b shows how a multiplexer is implemented by changing the content of the ME. The MEs are exposed to the software level to offer full controls over the functionality of the SWs at runtime.

## Slide 10: Conventional Switch

## Slide 11: XSwitch
Switch
North
East
West
South
Local
1
0
1
0
1
0
1
0
7
6
5
4
3
2
1
0
Up_Flip
Up_Address
Up_Data
Sel_Flip
In_East
In_South
In_Local
Wr. Addr
Wr. Data
D
Out_East
Addr[0]
Addr[1]
Addr[2]
3’bxx1
 1, 3, 5, 7
1
1
0
0
1
1
0
0
Notes: Unlike the conventional 5-port switch which is implemented by multiplexers with configurable selectors, our XSwitch is designed from a different point of view. Fig. 4 depicts the architecture of our XSwitch. We make use of the intrinsic idea of FPGA in implementing digital circuits using arrays of small memory elements (MEs) (lookup-table in Xilinx FPGA). As shown in Fig. 4a, there is one set of N 5-input MEs per output direction per output bit. The inputs are
from the North, East, West, South and Local ports. They are connected to the asynchronous address read port of the ME. The output port, connected to the read data output, is therefore the result of any 5-input combinational circuit. Multiplexer is just one of them. Fig. 4b shows how a multiplexer is implemented by changing the content of the ME. The MEs are exposed to the software level to offer full controls over the functionality of the SWs at runtime.

## Slide 12: Multicast with feedback
SW00
SW10
SW20
NI00
NI10
NI20
SW01
SW11
SW21
NI01
NI11
NI21
SW02
SW12
SW22
NI02
NI12
NI22
SW03
SW13
SW23
NI03
NI13
NI23
1
1
0
0
0
0
0
0
7
6
5
4
3
2
1
0
In_FB_East
In_FB_South
In_FB_Local
Out_FB_Local
3’b11x
 6, 7
In_FB_East
In_FB_South
Out_FB_Local

## Slide 13: Conventional-extended Switch

## Slide 14: Activate Connection
SW00
SW10
SW20
NI00
NI10
NI20
SW01
SW11
SW21
NI01
NI11
NI21
SW02
SW12
SW22
NI02
NI12
NI22
SW03
SW13
SW23
NI03
NI13
NI23
Notes: Modifying path. PEs are attached to NIs and are numbered after their SW. PE00→PE03 is the path from PE00 to PE03. There are 4 time slots represented by 4 arrows. One more time slot is requested for PE00→PE03 to increase the bandwidth.
the reconfiguration process in the aforementioned NoCs is based on the assumption that it does not overlap with the data transfer. This is not the case in a scenario when the user changes from a low quality video to a higher one. The bandwidth of the existing path needs to be adjusted as shown in Fig. 1. This example is elaborated in Section III-D

## Slide 15: Activate Connection
Notes: After that, the Master Proc decides whether to activate
the new path for PE10→PE13 or the additional time slot for
PE00→PE03. Suppose it does the latter first. The activating
process is demonstrated in Fig. 5b. Similar to the deactivating
process, the Control Unit only starts when the global Time Slot
is one slot ahead of the desired slot, in this case, 0. What it
does are to (1) flip the signal Flip Table to switch to the new
configuration and (2) activate the NIs/SWs. As shown, the new
slot is assigned to PE00→PE03 while the data is still flowing
between the PEs/SWs and the order of the data is not affected.
Likewise, the new path for PE10→PE13 is activated.

## Slide 16: Activate Connection

## Slide 17: Activate Connection

## Slide 18: Activate Connection

## Slide 19: Activate Connection

## Slide 20: Activate Connection

## Slide 21: Activate Connection
Activate Slot 1

## Slide 22: Activate Connection
Activate Slot 2

## Slide 23: Activate Connection
Activate Slot 3

## Slide 24: Activate Connection
Activate Slot 0

## Slide 25: Activate Connection
Activate Slot 2

## Slide 26: Activate Connection

## Slide 27: Activate Connection

## Slide 28: Deactivate Connection

## Slide 29: Deactivate Connection

## Slide 30: Contributions
Features | [1,2,3] | [4,5] | XNoC
Controller | Centralized | Decentralized | Distributed
Multicast with aggregated feedback | × | × | 
Non-intrusive reconfiguration | × | × | 
Reconfiguration Latency | × |  | 
Scalability | × |  | 
[1] Goossens, K., Dielissen, J. & Radulescu, A., Æthereal network on chip: concepts, architectures, and implementations. Design & Test of Computers, IEEE, 2005
[2] Hansson, A., Subburaman, M. & Goossens, K., 2009. aelite: A flit-synchronous network on chip with composable and predictable services. In DATE 2009
[3] Stefan, R.A., Molnos, A. & Goossens, K., 2014. dAElite: A TDM NoC supporting qos, multicast, and fast connection set-up. IEEE Transactions on Computer, 2014
[4] Liu, S., Jantsch, A. & Lu, Z., 2014. Parallel probe based dynamic connection setup in TDM NoCs. In DATE 2014
[5] Lusala, A.K. & Legat, J.-D., 2012. A SDM-TDM-Based Circuit-Switched Router for On-Chip Networks. ACM TRETS 2012
Notes: The disadvantages of using decentralized compared to centralized control unit in [15], [16] are (1) it cannot establish a multi-cast domain because the sender needs to wait for the acknowledged signals from all receivers to make sure that the paths are setup; the control units would become much more complex to handle the responses from the neighbors; (2) the routing algorithm cannot be changed at runtime unless the routers are partially reconfigurable; (3) it does not have the global view of the current state of the network to adapt to changes at runtime; (4) it only allocates one slot for one path at a time; there is no guarantee that the data in multi-time-slot path arrive at the destination in order.
- The most concerned problem of CSw NoC with centralized control unit is the path setup and tear-down overhead. They can be over 1000 clock cycles in [12] or about 100 cycles for one short path in [14]. Having a predictable path setup/teardown latency as low as possible is the first step in making it feasible to interleave multiple paths that share the same links and time slots. It is similar to the context switching in multithreaded software environment. Another drawback of conventional centralized control unit is scalability. For large NoCs with hundreds or even thousand of PEs, the reconfiguration process becomes a bottleneck. Moreover, having the control links span the whole network severely affects the timing of the design. One may insert the buffers along the links but it again increases the reconfiguration latency.

## Slide 31: Distributed Control Plane
31
SW00
SW10
SW20
SW01
SW11
SW21
SW02
SW12
SW22
NI00
NI10
NI20
NI01
NI11
NI21
NI02
NI12
NI22
SW03
SW13
SW23
NI02
NI12
NI22
SW30
SW31
SW32
NI30
NI31
NI32
SW33
NI33
Centralized Controller
Processor

## Slide 32: Distributed Control Plane
SW00
SW10
SW01
SW11
NI00
NI10
NI01
NI11
SW02
SW12
NI02
NI12
SW03
SW13
NI02
NI12
SW20
SW21
NI20
NI21
SW30
SW31
NI30
NI31
SW22
NI22
SW23
NI22
SW32
NI32
SW33
NI33
Sub-Ctrl 00
Sub-Ctrl 10
Sub-Ctrl 01
Sub-Ctrl 11
Control Agent
Processor
Strict Sync.
Out-of-Order Sync.

## Slide 33: Sub-Controller Synchronization
Strict Synchronization
Out-of-Order Synchronization

## Slide 34: Experiments
Resource cost of XSwitch
Resource cost of XNoC
  Xilinx ISE 14.7 - Virtex-6 XC6VLX240T
  Altera Quartus II 11.0sp1 - Stratix III EP3SL340F
Speedup gained from Distributed Control Plane
  SystemC simulation

## Slide 35: Resource Cost - XSwitch
Chart: Slices (Log Scale)
| Conv SW | Xswitch | Conv-Ex Sw | Conv SW | Xswitch | Conv-Ex Sw | Conv SW | Xswitch | Conv-Ex Sw | Conv SW | Xswitch | Conv-Ex Sw | Conv SW | Xswitch | Conv-Ex Sw | Conv SW | Xswitch | Conv-Ex Sw | 1 | 2 | 4 | 8 | 16 | 32
4 Slots | 2 | 4 | 39 | 2 | 5 | 58 | 4 | 11 | 124 | 6 | 21 | 248 | 10 | 40 | 511 | 18 | 78 | 915
8 Slots | 2 | 7 | 27 | 2 | 11 | 77 | 4 | 21 | 114 | 6 | 41 | 233 | 10 | 80 | 448 | 18 | 161 | 1039
16 Slots | 2 | 10 | 32 | 2 | 20 | 62 | 3 | 38 | 101 | 5 | 75 | 203 | 10 | 146 | 500 | 18 | 289 | 1040
32 Slots | 2 | 21 | 43 | 2 | 37 | 57 | 3 | 71 | 103 | 6 | 138 | 217 | 10 | 277 | 481 | 18 | 547 | 758
3.5X
Notes: XSwitch is a better alternative to the conventional 5-input multiplexer-based SWs (Conv SW). Any 5-input combinational circuit can be implemented in the XSwitch to perform the reduction operations without any extra resource. Besides, every output bit of the XSwitch can be configured independently. For example, the first bit of the North output port selects the input from the West port while the second bit selects the input from the South port.
Therefore, to have a fair comparison of the XSwitch with the Conv SW, we implement the Conv-Ex SW. It is the extension of the Conv SWs with the same features as the XSwitch. Fig. 10 shows the resource consumptions of these SWs.
As expected, the XSwitch takes more resources than the Conv SW. Nevertheless, on the average, the resource requirement of the XSwitch is 3.5 times lower than the Conv-Ex SW.
However, we only implement 5 configurable combinational circuits for the Conv-Ex SW which are AND, NAND, OR, NOR and XOR. The cost of the XSwitch is expected to be much better than the Conv-Ex SW when more combinational circuits are integrated into the Conv-Ex SW.
It is worth noting that in the Conv SWs, the structure of the multiplexer is fixed, the selector is configurable by using a 3-bit wide memory. This memory consumes only 2 slices for up to 64-word depth. Thus, the resource cost of the Conv SWs varies insignificantly when the ping-pong technique is utilized (Section III-B). In contrast, in the XSwitch, the multiplexer is just one of the combinational functions realized by the MEs. If the ping-pong technique is used, the resources will be doubled. Therefore, in this current implementation, we decide to utilize the hybrid approach to inherit all the benefits of both SWs, i.e, the Conv SW is used for the data path (to save the resource) and the XSwitch is used for the feedback path (to support the reduction operations).

## Slide 36: XNoC with Different Configurations
Chart: Number of Slice
| 2x2 | 2x3 | 3x3 | 3x4 | 4x4 | 4x5 | 5x5 | 5x6 | 6x6
4 Slots | 323.75 | 331 | 951 | 955.25 | 1861.5 | 1856.75 | 3069 | 3074.75 | 4559
8 Slots | 357.5 | 364 | 1041.5 | 1045.75 | 2025.5 | 2030.5 | 3353.5 | 3359.25 | 4982.75
16 Slots | 426 | 434.75 | 1225.75 | 1230 | 2380.25 | 2385.25 | 3933.75 | 3979 | 5843.75
32 Slots | 550.75 | 561 | 1572.5 | 1576.75 | 3048.5 | 3043.5 | 5026.75 | 5072 | 7438.5
Notes: the data width is 32-bit and the feedback signal is 1-bit wide. The synthesis process is configured to optimize the area.
the resource cost increases almost linearly with its size.
the size of the XNoC has a little effect on the maximum achievable frequency. It only drops 1.5% when the number of nodes is more than 16

## Slide 37: XNoC Compared to Others
Chart: Number of Slices
| 2x2, 8-slot, 39-bit link, area opt. | 2x2, 8-slot, 39-bit link, timing opt. | 2x2, 32-slot, 39-bit link, area opt. | 2x2, 32-slot, 39-bit link, timing opt.
XNoC | 3073 | 3639 | 3470 | 4313
dAElite [1] | 3098 | 3655 | 3483 | 4425
aelite [2] | 5500 | 5393
[1] Stefan, R.A., Molnos, A. & Goossens, K., 2014. dAElite: A TDM NoC supporting qos, multicast, and fast connection set-up. IEEE Transactions on Computer, 2014
[2] Hansson, A., Subburaman, M. & Goossens, K., 2009. aelite: A flit-synchronous network on chip with composable and predictable services. In DATE 2009
Notes: Since different NoCs have different features and architectures, it is difficult to compare them directly. Additionally, some works only report the ASIC implementation results. Therefore, we only compare our work against the ones which are similar to ours and are implemented on FPGA.
shows the place and route results of XNoC in comparison with dAElite [14] and aelite [13] with the same configurations.
The major difference between our current implementation and the closest NoC, dAElite, is the NI. Currently, we employ the AXI-Stream interface for NI. The mapping from different addresses to specific time slots is not yet supported. However, we did project the expected resources of XNoC with fullfeatured NIs based on the resource break-down information provided in [14].
As seen, XNoC requires less resources than dAElite while offering more features. The minimum clock period of XNoC is also better,
In TDM CSw NoCs, the throughput of a connection is always guaranteed once it is set up. It only depends on the number of assigned time slots and the clock speed of the NoC. Therefore, 50% improvement in clock speed can be translated to 50% faster throughput.
It is worth noting that XNoC’s timing performance should not be affected by the full-featured NIs once implemented. It is because there are always buffers between NIs and SWes inside NoC to store the packets. These buffers set apart the path from NI to SW and SW to NoC. As a result, the NI would be able to operate at a frequency different from the NoC.
Additionally, the aeltie consumes much more resources than XNoC. The reason is that it requires a translator at each NI to decode/encode the configuration data on the regular network channels to update its path tables. In XNoC, the paths are embedded inside the MEs of the XSwitch and they are updated directly by the Control Unit or SubCtrls.

## Slide 38: XNoC Compared to Others
Chart: MHz
| 2x2, 8-slot, 39-bit link, area opt. | 2x2, 8-slot, 39-bit link, timing opt. | 2x2, 32-slot, 39-bit link, area opt. | 2x2, 32-slot, 39-bit link, timing opt.
XNoC (clk) | 246.4876 | 250.941 | 210.3934 | 250.7523
dAElite [1] (clk) | 122.1001 | 201.2882 | 113.1222 | 206.1856
aelite [2] (clk) | 119.346 | 200.5616
[1] Stefan, R.A., Molnos, A. & Goossens, K., 2014. dAElite: A TDM NoC supporting qos, multicast, and fast connection set-up. IEEE Transactions on Computer, 2014
[2] Hansson, A., Subburaman, M. & Goossens, K., 2009. aelite: A flit-synchronous network on chip with composable and predictable services. In DATE 2009
2X
Notes: Since different NoCs have different features and architectures, it is difficult to compare them directly. Additionally, some works only report the ASIC implementation results. Therefore, we only compare our work against the ones which are similar to ours and are implemented on FPGA.
shows the place and route results of XNoC in comparison with dAElite [14] and aelite [13] with the same configurations.
The major difference between our current implementation and the closest NoC, dAElite, is the NI. Currently, we employ the AXI-Stream interface for NI. The mapping from different addresses to specific time slots is not yet supported. However, we did project the expected resources of XNoC with fullfeatured NIs based on the resource break-down information provided in [14].
As seen, XNoC requires less resources than dAElite while offering more features. The minimum clock period of XNoC is also better,
In TDM CSw NoCs, the throughput of a connection is always guaranteed once it is set up. It only depends on the number of assigned time slots and the clock speed of the NoC. Therefore, 50% improvement in clock speed can be translated to 50% faster throughput.
It is worth noting that XNoC’s timing performance should not be affected by the full-featured NIs once implemented. It is because there are always buffers between NIs and SWes inside NoC to store the packets. These buffers set apart the path from NI to SW and SW to NoC. As a result, the NI would be able to operate at a frequency different from the NoC.
Additionally, the aeltie consumes much more resources than XNoC. The reason is that it requires a translator at each NI to decode/encode the configuration data on the regular network channels to update its path tables. In XNoC, the paths are embedded inside the MEs of the XSwitch and they are updated directly by the Control Unit or SubCtrls.

## Slide 39: XNoC Compared to Others
Chart: ALUT
| XNoC: 4x4, 16-slot, 54-bit link [3]: 4x4, 3 18-bit lanes, 5-slot | XNoC: 4x4, 16-slot, 90-bit link [3]: 5 18-bit lanes, 3-slot
XNoC | 68454 | 71698
SDM-TDM [3] | 70815 | 90141
[3] Lusala, A.K. & Legat, J.-D., 2012. A SDM-TDM-Based Circuit-Switched Router for On-Chip Networks. ACM TRETS 2012
Notes: The synthesis results of XNoC on the Altera Stratix III EP3SL340F (using Quartus II 11.0sp1) are also presented to compare with [16]. The resource cost of XNoC is slightly lower than SDM-TDM in the 3-lane-5-slot configuration and much lower in the 5-lane-3-slot configuration.
In both cases, the reported Fmax for XNoC is almost 3 times better than SDM-TDM thanks to the simple Xswitch architecture and the update mechanism.

## Slide 40: XNoC Compared to Others
Chart: MHz
| XNoC: 4x4, 16-slot, 54-bit link [3]: 4x4, 3 18-bit lanes, 5-slot | XNoC: 4x4, 16-slot, 90-bit link [3]: 5 18-bit lanes, 3-slot
XNoC | 292 | 296
SDM-TDM [3] | 90 | 102
[3] Lusala, A.K. & Legat, J.-D., 2012. A SDM-TDM-Based Circuit-Switched Router for On-Chip Networks. ACM TRETS 2012
3X
Notes: The synthesis results of XNoC on the Altera Stratix III EP3SL340F (using Quartus II 11.0sp1) are also presented to compare with [16]. The resource cost of XNoC is slightly lower than SDM-TDM in the 3-lane-5-slot configuration and much lower in the 5-lane-3-slot configuration.
In both cases, the reported Fmax for XNoC is almost 3 times better than SDM-TDM thanks to the simple Xswitch architecture and the update mechanism.

## Slide 41: Distributed Control Plane
Instead of fully randomizing the connection (de)-activation requests, the locality value is introduced to model the behavior of the requests better.
The larger the locality, the higher the chance the connections are not crossing multiple regions.
Notes: In this section, the performance of the XNoC with distributed control plane is compared against the XNoC with centralized approach. The performance is characterized in terms of speedup in different network setting
When the number of SubCtrls increases, the number of PEs in each physical region reduces. It becomes harder for the communication aware runtime application mapping algorithm to find a feasible mapping if it is only restricted to the available PEs in one region. Thus, we also define communication regions. These regions are superimposed over the physical ones as follows: 1x2 for 1x2 SubCtrls, 1x2 for 2x2 SubCtrls, 2x2 for 2x4 SubCtrls, and 2x2 for 4x4 SubCtrls.

## Slide 42: Speedup
Chart: Locality
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
1x2 - No OOO | 1.3774 | 1.3573 | 1.3353 | 1.3047 | 1.2956 | 1.2928 | 1.2925 | 1.3051 | 1.3496 | 1.4361 | 1.9508
2x2 - No OOO | 1.8189 | 1.8125 | 1.8087 | 1.7769 | 1.7454 | 1.7763 | 1.7779 | 1.7714 | 1.8536 | 1.9939 | 2.6591
2x4 - No OOO | 2.3148 | 2.3465 | 2.33 | 2.3135 | 2.4316 | 2.4189 | 2.4799 | 2.5443 | 2.8048 | 3.0112 | 4.7389
4x4 - No OOO | 3.4669 | 3.458 | 3.443 | 3.458 | 3.5133 | 3.5424 | 3.5773 | 3.6445 | 4.0734 | 4.4354 | 6.4107
1x2 - OOO | 1.4651 | 1.4571 | 1.4403 | 1.4101 | 1.4184 | 1.4099 | 1.4048 | 1.4148 | 1.4473 | 1.5503 | 1.9509
2x2 - OOO | 2.101 | 2.1103 | 2.1232 | 2.1204 | 2.0616 | 2.1092 | 2.0811 | 2.1005 | 2.1552 | 2.3049 | 2.8445
2x4 - OOO | 3.0718 | 3.1057 | 3.0948 | 3.0847 | 3.1843 | 3.1661 | 3.2324 | 3.2824 | 3.4328 | 3.687 | 5.1366
4x4 - OOO | 4.8268 | 4.9461 | 4.8063 | 4.8778 | 5.0158 | 5.0719 | 5.0589 | 5.0923 | 5.4328 | 5.8394 | 7.5943
Notes: presents the speedup achieved from the 32x32 XNoC with different number of SubCtrls and minimum instruction buffer size.
The instructions are written directly to SubCtrls by Master Proc.

## Slide 43: Connection Activation Latency
Chart: Clock cycles
| 6 Hops | 8 Hops | 10 Hops | 12 Hops
dAElite [1] | 81 | 94 | 119 | 133
Par. Probe [2] | 208 | 240 | 272 | 304
XNoC - Cent. | 136 | 152 | 168 | 184
XNoC - Dist. | 37 | 49 | 62 | 74
[1] Stefan, R.A., Molnos, A. & Goossens, K., 2014. dAElite: A TDM NoC supporting qos, multicast, and fast connection set-up. IEEE Transactions on Computer, 2014
[2] Liu, S., Jantsch, A. & Lu, Z., 2014. Parallel probe based dynamic connection setup in TDM NoCs. In DATE 2014

## Slide 44: Conclusion
XNoC architecture with XSwitch
Multicast with aggregated feedback
Connection activation process
Distributed control plane

## Slide 45: Thank You!

## Slide 46: Apendix

## Slide 47: Contributions
Non-intrusive reconfiguration
Low latency and predictable path (de)-activation
Multicast service with aggregate feedback
Distributed control plane for scalability

## Slide 48: Data Injection Latency
Chart: Clock cycles
| 6 Hops | 8 Hops | 10 Hops | 12 Hops
dAElite [1] | 89 | 103 | 127 | 141
Par. Probe [2] | 34 | 38 | 42 | 46
XNoC - Cent. | 10 | 10 | 10 | 10
XNoC - Dist. | 13 | 14 | 16 | 17
[1] Stefan, R.A., Molnos, A. & Goossens, K., 2014. dAElite: A TDM NoC supporting qos, multicast, and fast connection set-up. IEEE Transactions on Computer, 2014
[2] Liu, S., Jantsch, A. & Lu, Z., 2014. Parallel probe based dynamic connection setup in TDM NoCs. In DATE 2014

## Slide 49: XSwitch – Micro-arch
Dual-port RAM
3’bxx1
 1, 3, 5, 7
Notes: Unlike the conventional 5-port switch which is implemented by multiplexers with configurable selectors, our XSwitch is designed from a different point of view. Fig. 4 depicts the architecture of our XSwitch. We make use of the intrinsic idea of FPGA in implementing digital circuits using arrays of small memory elements (MEs) (lookup-table in Xilinx FPGA). As shown in Fig. 4a, there is one set of N 5-input MEs per output direction per output bit. The inputs are
from the North, East, West, South and Local ports. They are connected to the asynchronous address read port of the ME. The output port, connected to the read data output, is therefore the result of any 5-input combinational circuit. Multiplexer is just one of them. Fig. 4b shows how a multiplexer is implemented by changing the content of the ME. The MEs are exposed to the software level to offer full controls over the functionality of the SWs at runtime.

## Slide 50: XSwitch - Schematic
Dual-port RAM

## Slide 51: Multicast
3’b11x
 6 and 7
3’b1x1
 5 and 7
Notes: In XNoC, since the XSwitch can implement any 5-input combinational circuit for a particular output, aggregating feedback signal becomes trivially doable. In Fig. 2, SW00 performs the bit-wise AND operation to the feedbacks from SW10 and SW01 before forwarding them to the NI00. This can be denoted as follows: Out Local = In South ∧ In East. Similarly, at SW02: Out West = In Local ∧ In East. Fig. 6 shows the corresponding data for the MEs at SW00 and
SW02. In other words, the MEs are the truth tables of any one-output combinational circuit of five inputs. Besides, the aggregation only performs as intended when the feedbacks from the receiving nodes arrive at the SWs at the same time slot. This condition is easily satisfied if the schedule of the feedbacks follows Equation 6. The time taken by the aggregated feedback to propagate to the source node equals to the longest path from the source node to the sink nodes

## Slide 52: Feedback Signal Scheduling

## Slide 53: Sub-Controller Strict Synchronization

## Slide 54: Sub-Controller Out-of-Order Configuration

## Slide 55: Effect of Feedback on Routing

## Slide 56: Effect of Feedback on Routing

## Slide 57: Activate Connection
Activate
Slot 1
Activate
Slot 2
Activate Slot 3
Activate
Slot 0
Activate
Slot 1
Notes: After that, the Master Proc decides whether to activate
the new path for PE10→PE13 or the additional time slot for
PE00→PE03. Suppose it does the latter first. The activating
process is demonstrated in Fig. 5b. Similar to the deactivating
process, the Control Unit only starts when the global Time Slot
is one slot ahead of the desired slot, in this case, 0. What it
does are to (1) flip the signal Flip Table to switch to the new
configuration and (2) activate the NIs/SWs. As shown, the new
slot is assigned to PE00→PE03 while the data is still flowing
between the PEs/SWs and the order of the data is not affected.
Likewise, the new path for PE10→PE13 is activated.

## Slide 58: Deactivate Connection

## Slide 59: XNoC – Control vs Data Links

## Slide 60: XNoC Compared with Others
NoC Configuration | XNoC | Others
2x2, 8-slot, 39-bit link, area opt. | 3073 (488) slices, 4057 ps | [1] 3098 Slices, 8190 ps
 |  | [2] 5500 slices, 8379 ps
2x2, 8-slot, 39-bit link, timing opt. | 3639 (581) slices, 3985 ps | [1] 3655 slices, 4968 ps
 |  | [2] 5393 slices, 4986 ps
2x2, 32-slot, 39-bit link, area opt. | 3470 (697) slices, 4753 ps | [1] 3483 slices, 8840 ps
2x2, 32-slot, 39-bit link, timing opt. | 4313 (777) slices, 3988 ps | [1] 4425 slices, 4850 ps
[XNoC] 4x4, 16-slot, 54-bit link [3] 4x4, 3 18-bit lanes, 5-slot | 68454 ALUTs, 292 MHz | [3] 70815 ALUTs, 90 MHz
[XNoC] 4x4, 16-slot, 90-bit link [3] 4x4, 5 18-bit lanes, 3-slot | 71698 ALUTs, 296 MHz | [3] 90141 ALUTs, 102 MHz
Notes: Since different NoCs have different features and architectures, it is difficult to compare them directly. Additionally, some works only report the ASIC implementation results. Therefore, we only compare our work against the ones which are similar to ours and are implemented on FPGA. Table I shows the place and route results of XNoC in comparison with dAElite [14] and aelite [13] with the same configurations. The synthesis results of XNoC on the Altera Stratix III EP3SL340F (using Quartus II 11.0sp1) are also presented to compare with [16]. The major difference between our current implementation and the closest NoC, dAElite, is the NI. Currently, we employ the AXI-Stream interface for NI. The mapping from different addresses to specific time slots is not yet supported. However, we did project the expected resources of XNoC with fullfeatured NIs based on the resource break-down information provided in [14]. In Table I, the numbers in parentheses are the slice resources of XNoC without the full-featured NIs.
As seen, XNoC requires less resources than dAElite while offering more features. The minimum clock period of XNoC is also better, which is up to 50% better than dAElite. In TDM CSw NoCs, the throughput of a connection is always guaranteed once it is set up. It only depends on the number of assigned time slots and the clock speed of the NoC. Therefore, 50% improvement in clock speed can be translated to 50% faster throughput. It is worth noting that XNoC’s timing performance should not be affected by the full-featured NIs once implemented. It is because there are always buffers between NIs and SWes inside NoC to store the packets. These buffers set apart the path from NI to SW and SW to NoC. As a result, the NI would be able to operate at a frequency different from the NoC.
Additionally, the aeltie consumes much more resources than XNoC. The reason is that it requires a translator at each NI to decode/encode the configuration data on the regular network channels to update its path tables. In XNoC, the paths are embedded inside the MEs of the XSwitch and they are updated directly by the Control Unit or SubCtrls.
The resource cost of XNoC is slightly lower than [16] in the 3-lane-5-slot configuration and much lower in the 5-lane-3-slot configuration. In both cases, the reported Fmax for XNoC is almost 3 times better than [16] thanks to the simple Xswitch architecture and the update mechanism.

## Slide 61: Connection Activation Latency
Works | 6 Hops | 8 Hops | 10 Hops | 12 Hops
dAElite [14] | 81 (89) | 94 (103) | 119 (127) | 133 (141)
Paralel Probe [15] | 208 (34) | 240 (38) | 272 (42) | 304 (46)
XNoC – Centralized | 136 (10) | 152 (10) | 168 (10) | 184 (10)
XNoC – Distributed | 37 (13) | 49 (14) | 62 (16) | 74 (17)

## Slide 62: Distributed Control Plane Conservative Synchronization

## Slide 63: Distributed Control Plane Out-of-Order Configuration

## Slide 64: Speedup – Write Req. Indirectly
Notes: All connection (de)-activation (for both data and feedback) and the corresponding SW reconfiguration requests are generated based on the uniformly randomly chosen source and destination nodes.

## Slide 65: Speedup – Write Req. Directly
Notes: All connection (de)-activation (for both data and feedback) and the corresponding SW reconfiguration requests are generated based on the uniformly randomly chosen source and destination nodes.

## Slide 66: Speedup – Write Req.
Write Req. Via Control Agent
Write Req. Directly to Sub-Ctrl
Notes: All connection (de)-activation (for both data and feedback) and the corresponding SW reconfiguration requests are generated based on the uniformly randomly chosen source and destination nodes.

## Slide 67: Connection Activation Latency
Notes: The average number of clock cycles required to activate connections in a 32x32 XNoC with default settings is reported the average and maximum requested number of time slots is 8 and 16 respectively. The lengths of connections range from 10 to 26.
The results are calculated by dividing the time needed to activate a connection by its length and the requested number of time slots. The SWs reconfiguration time is not included because they can be hidden by the on-going data communication in the network.
This experiment is carried out based on the scenario where there are back-to-back connection activation requests generated by the Master Proc. In this case, the parallelism of distributed control plane is well exploited

## Slide 68: Distributed Control Plane
SW00
SW10
SW01
SW11
NI00
NI10
NI01
NI11
SW02
SW12
NI02
NI12
SW03
SW13
NI02
NI12
SW20
SW21
NI20
NI21
SW30
SW31
NI30
NI31
SW22
NI22
SW23
NI22
SW32
NI32
SW33
NI33

## Slide 69: Distributed Control Plane
69
SW00
SW10
SW20
SW01
SW11
SW21
SW02
SW12
SW22
NI00
NI10
NI20
NI01
NI11
NI21
NI02
NI12
NI22
SW03
SW13
SW23
NI02
NI12
NI22
SW30
SW31
SW32
NI30
NI31
NI32
SW33
NI33

## Slide 70: Distributed Control Plane
Notes: As discussed in Section II-B, the centralized control unit cannot scale well with large networks. In this section, a distributed control plane is presented to handle such networks. Fig. 7 shows our control plane with 4 Sub-Controllers (SubCtrls). Each SubCtrl manages one sub-region of the network. The Control Agent forwards the instructions received from the Master Proc to the respective SubCtrl to reconfigure the SWs or (de)-activate the paths. The Control Agent is also responsible for synchronizing the SubCtrls in some specific operations. In our architectural model, we adopt the centralized management system [3], [4]. The Master Proc has the knowledge of the current status of the system as well as the privilege of managing the applications, loading the partial bitstreams to the PEs and reconfiguring the network. The Master Proc is
not necessarily a single core processor nor a single processor;
it can be a multi-core processor or a set of processors in
the runtime management domain. Therefore, the bottleneck of
generating the configurations for the large system at runtime
is not a big concern.